IRS-1C/1D/P6

DIGITAL DATA PRODUCTS FORMAT

FOR REVISION C FAST FORMAT PRODUCTS

May, 2003

Data Products Software Division

Signal and Image Processing Group

Space Applications Center,ISRO,Ahmedabad – 380 015

DOCUMENT CONTROL AND DATA SHEET

1.	Report No. and date:	IRS-P6/DP/SAC/SIIPA/SIPG/TN-05/MAY 2002

2.	Title and sub-title: 	IRS-1C/1D/P6 DIGITAL DATA PRODUCTS FORMAT

FOR REVISION C FAST FORMAT PRODUCTS

3.	Type of Report	 : 	TECHNICAL

- No. of pages       :	26

5.	Authors		 : 	Sk.Sazid Mahammad,

IRS DATA PRODUCTS TEAM

SIPG GROUP

SPACE APPLICATION CENTRE

AHMEDABAD

6.	Abstract		 :	THIS DOCUMENT CONTAINS THE FORMAT FOR

IRS-1C/1D/P6 FAST FORMAT DIGITAL DATA

PRODUCTS

7.	Key words		 : 	FAST FORMAT, HEADER FILE,IMAGE FILE,

BLOCKED RECORD,ADMINISTRATIVE RECORD,

RADIOMETRIC RECORD, GEOMETRIC RECORD,

MAP PROJECTIONS, FORMAT LAYOUTS.

8.	Security

Classification	 : 	UNRESTRICTED

IRS-1C/1D/P6

DIGITAL DATA PRODUCTS FORMAT

FOR REVISION C FAST FORMAT PRODUCTS

TABLE OF CONTENTS

1.0 INTRODUCTION	4

1.1 GENERAL FORMAT RULES	4

1.2 GENERAL FORMAT DESCRIPTION	4

1.2.1 HEADER FILE	4

1.2.2 IMAGE FILES	5

1.2.3 BLOCKED RECORDS	5

2.0 DETAILED FORMAT DESCRIPTION 2.1 HEADER FILES	5

2.1.1 ADMINISTRATIVE RECORD	5

2.1.2 RADIOMETRIC RECORD	7

2.1.3 GEOMETRIC RECORD	7

2.2 SOFTWARE :	9

APPENDIX-A :  Map Projections	10

APPENDIX- B-1 : Earth Ellipsoids	11

APPENDIX- B-2: Ellipsoid and Datum Mnemonics	12

APPENDIX – C : USGS    Projection Parameters	13

APPENDIX-D : Fast Format Header File Record Format Tables	16

APPENDIX-E : Fast Format Layout	26

IRS-1C/1D/P6

DIGITAL DATA PRODUCTS FORMAT

FOR REVISION C FAST FORMAT PRODUCTS

# 1.0 INTRODUCTION

This document describes the format for IRS-1C/1D/P6 fast format digital data products.

## 1.1 GENERAL FORMAT RULES

1. All field definitions strictly follow American National Standard Institute (ANSI) and International Organization for Standardization (ISO) standards.

2. Only Band Sequential (BSQ) image structure is supported because data to be written to tape is made available a single band at a time .

3. Image files consist of a single band of data.

4. A digital product is referred to as a volume set. Individual media (8mm DAT, CD) are   referred to as volumes.  A volume set may have one or more volumes, depending on image size and output media capacity.

## 1.2 GENERAL FORMAT DESCRIPTION

The Fast Format (Version C) volume set contains a Header File and Image Files.

### 1.2.1 HEADER FILE

The first file on each volume, a Read-Me-First file, contains header data.  It is in American Standard Code for Information Interchange (ASCII) format, confirming to ANSI and ISO standards.

Alphanumeric fields are left justified and numeric fields are right justified.  Dates are given in yyyy ddmm format (full year, day-of-month and month format).  All processing options, radiometric calibration, geometric characteristics and map projection information for the product are contained in this file.  Appendix D contains a table of the entries in the Header File.  The table breaks the information into 80 byte units with a carriage return as the eightieth character, allowing convenient printing of the file.  For this reason, each 80 byte unit is referred to as a line.  The table lists the field number in each record, the start and stop byte number, a FORTRAN format representation and a short text describing the field contents.

### 1.2.2 IMAGE FILES

Each image file contains one band of image data.  There are no header records within the image file, nor are there prefix and/or suffix data in the individual image records.  Image data may be blocked or unblocked.

### 1.2.3 BLOCKED RECORDS

This blocking results in writing fewer End-of-Record gaps on the tape and allows more data to be written to the tape.

## 2.0 DETAILED FORMAT DESCRIPTION

## 2.1 HEADER FILES

The Header File contains three 1536-byte ASCII records.  The first record is the Administrative Record which contains information that identifies the product, the scene and the data specifically needed to ingest the imagery from the digital media.   In order to import the image data, it is necessary to read entries in the Administrative Record.

The second record is the Radiometric Record which contains the coefficients needed to convert the scene digital values into at-satellite spectral radiance.

The third record is the Geometric Record which contains the scene geodetic location information.  In order to align the imagery to other data sources, it will be necessary to read entries in the Geometric Record.

The accompanying tables in Appendix D describe the format of the three records, including the number of bytes, the FORTRAN format statement and a brief description of each field in the header file.  All alphanumeric fields are left justified, and all numeric fields right justified.  Fields of fixed (constant) values are represented with capital letters in quotes (e.g., "PRODUCT=").  Variable fields are represented with lower case letters.  In both fixed and variable fields, blank spaces are indicated by the lower case"b" character.

All three records in the Header File have a carriage return every eightieth character.

### 2.1.1 ADMINISTRATIVE RECORD

The first field in this record contains the Product ID, a unique identifier for the product as ordered by the customer.

The remainder of the initial two lines in this record describe the source of the image with pertinent sensor parameters.  The next six lines are replicates of the first two without the Product ID.  These are growth regions allowing for mosaic products containing up to four images and co-registered Panchromatic and multi-spectral imagery.  These products are proposed and but not yet implemented.

Line nine describes the type of product contained on the media i.e., size and orientation.  Line ten describes the characteristics of the processing: i.e., level of geometric correction and resampler used.

The remainder of the Administrative Record contains the critical fields required to import the image data to computer memory.

For unblocked data (8mm and CD-ROM), ingest of the imagery requires knowledge of the contents of fields 83 (pixels per line), 85 (Line per Band on this volume), 87 (No. of lines in output image) and 105 (Bands Present).  It is necessary to count the number of non-blank entries in the Bands Present field to get the count of the number of bands.  Each character (byte) in this field will have an ASCII character with the band label, usually a number.  For IRS-1C/1D/P6 the values are 2, 3, 4, 5  for  LISS-3,2,3,4  for   LISS-4,3,4 for  WiFS  and 2,3,4,5   for    AWiFS    and       P for PAN .

The sequence terminates in a blank.

For blocked data, fields 91 (Start Line), and either 93 (Blocking Factor) or 95 (Record Length) and 87 (Number of lines in the output image) are also needed.  Note that the (blocked) record length is equal to the blocking factor times the number of pixels per line.  One may choose the parameter that best fits their system software interface.

Fields 79 and 81 (Volume #/# in Set) relate to which volume number in a set and field 100 indicates Bits per Pixel.  Field 73 (bytes 741-751) in Line 10 contains the level of processing that has been performed on the image.

| RAW | No corrections applied |
| --- | --- |
| RADIOMETRIC | Radiometric corrections only |
| SYSTEMATIC | Radiometric and geometric corrections using spacecraft system data only. |
| PRECISION | Radiometric and geometric corrections using spacecraft system data along with control points. |
| TERRAIN | Radiometric and geometric corrections using spacecraft system data, along with control points and digital elevation model (DEM) |

Field 75 (bytes 765-766) in Line 10 contains the resampling algorithm that has been applied to the image.

CC = Cubic convolution     NN = Nearest neighbour SI=Sinc16  KI=Kaiser

Field 83 (bytes 843-847) in Line 11 contains the number of image pixels on each image line of each image band on the tape.

Field 85 (bytes 865-869) in Line 11 contains the number of image lines per band on this volume (This is the number of lines in each image file for tapes containing one or more complete image files.).

Field 87 (Bytes 871-875) contains the number of image lines for the entire band (The band may be split across multiple volumes).  These are right-justified numeric fields.

Field 91 (bytes 895-899) in Line 12 identifies the first image line on this tape volume.  This is "b1" unless the tape is the second or higher numbered volume of a multi-volume set (e.g. fields 79 & 81 are "b2/b2").  In this case it is the line number in the complete image of the first image line on the tape ((nominally N/2 + 1 for two-tape sets, where N is the total number of lines in the image)).  This is a right-justified ASCII numeric field.

Field 93 (bytes 918-919) in Line 12 contains the blocking factor used to minimize the number of CCT tapes required to accommodate the image set.  This field is always "1" for 8mm tapes. (See Blocking Factor explanation under Image Files).

Field 95 (bytes 936-940) in Line 12 contains the physical tape record length.  The value is right justified in an ASCII numeric field.  The number of pixels (samples) per image line can be determined by dividing this field in the value in Field 93 or by directly reading field 83 (bytes 843-847). For two byte data like AwiFS (IRS-P6) Pixels = RecordLength/(BlockingFactor * BytesPerPixel). Field 100 (bytes 984-985) in Line 13 contains the integer number of bits per pixel that is used in the output media to represent the digital value of each individual pixel.  (This value may be different from Field 102).

Field 102 (bytes 1012-1013) in Line 13 contains the integer number of bits per pixel that each individual pixel was quantized the satellite instrument.  (This value may be different from field 100) IRS-1C panchromatic data is transmitted as six bit pixels, while the digital products are always produced are always produced with eight bit pixels.

Field 106 (bytes 1056-1087) in Line 14 contains the band identifiers for the image files on the tape volume.  This field is composed of thirty-two- one-byte sub-fields containing from one to thirty-two of the band identifies (i.e., "234b" for full IRS-1C LISS-3 data sets or "Pb" for IRS-1C panchromatic data sets).  The band identifiers are listed in the order in which the image files appear on the tape and are single character fields.  So the leftmost character (byte 1056) must be non-zero.  The sequence ends with trailing blanks.

### 2.1.2 RADIOMETRIC RECORD

Fields 4-41 (bytes 81-689) contains the coefficients needed to convert scene digital values to at-satellite spectral radiances.

Conversion formula for Digital Count to radiance is as follows.

Lrad = (DN/MaxGray)*(Lmax – Lmin) + Lmin.

Lrad            : Radiance for a given DN value.

DN              : Digital Count

MaxGray    : IRS-1C/1D : 63 for PAN & 127 for WiFS & LISS-3 for Raw Products only.

255 for Corrected products.

For IRS-P6 : 127 for LISS-4 and LISS-3, 1023 for AWiFS for raw products only.

255 for LISS-3&4,1023  for AWiFs for corrected products

Lmin/Lmax(Bias/Gain) : Minimum/Maximum radiance value for a given band supplied as bias and gain respectively.

### 2.1.3 GEOMETRIC RECORD

Line 1 contains the map projection (field 3), Earth ellipsoid (field 5) and datum (field 7) used in producing the product.  Appendix A contains the list of supported map projections and Appendix B contains the list of supported Earth ellipsoids and comments about the datum.  Products are not always available in all projections and ellipsoids.

Fields 11-44 (bytes 110-504, lines two to six) contain the USGS projection parameters used to process the image in standard USGS order.  The meaning of these values depends on the projection used.  For information about the contents of each of the map projection fields, see Appendix C. Fields 47-88 (bytes 561-859, lines eight to eleven) contain the corresponding corner pixel locations (longitude, latitude, easting, northing) relative to the resampled pixel center for all bands on the current tape volume.  Line twelve contains the same information about the scene center as well as the location of the scene center relative to the top right corner of the image on this medium.  To calculate the Northing and Easting of any pixel within the image, use the map coordinates of the image corner points and the following equations:

PE = ((NP-P)(NL-L)ULE+(P-1)(NL-L)URE+(NP-P)(L-1)LLE+(P-1)(L-1)LRE)/(NP-1)(NL-1))

PN = ((NP-P)(NL-L)ULN+(P-1)(NL-L)URN+(NP-P)(L-1)LLN+(P-1)(L-1)LRN)/(NP-1)(NL-1))

Where

| PE | Desired pixel location Easting |
| --- | --- |
| PN | Desired pixel location Northing |
| ULE | Upper left corner point Easting (Field 53) |
| URE | Upper right corner point Easting (Field 64) |
| LLE | Lower left corner point Easting (Field 86) |
| LRE | Lower right corner point Easting (Field 75) |
| ULN | Upper left corner point Northing (Field 55) |
| URN | Upper right corner point Northing (Field 66) |
| LLN | Lower left corner point Northing (Field 88) |
| LRN | Lower right corner point Northing (Field 77) |
| P | Pixel number of desired location (counted from left) |
| L | Line number of desired location (counted from top) |
| NP | Number of pixels per image line (Record 1, Field 83) |
| NL | Total number of lines in the output image (Record 1, Field 87) |

Field 107 (bytes 969-974) in Line thirteen contains the horizontal offset of the true scene center from the nominal scene center in units of whole pixels.  A negative value implies a westerly offset of the scene center from the nominal scene center in daytime scenes and an easterly offset of the scene center in nighttime scenes.

Field 109 (bytes 995-1000) in Line thirteen identifies the orientation angle of the scene.  For non-polar scenes the orientation angle of the scene is relative to the scene alignment to map or grid north.  For non polar map oriented scenes this field should be zero.  A negative angle implies a clockwise rotation of the scene to align with map north whereas a positive angle implies a counterclockwise rotation of the scene to align with map north.  To calculate the orientation angle of any image use the following equation:

| ANGLE | arctan (NORTHDIFE/EASTDIFF) |
| --- | --- |
| NORTHDIFF | URNORTH – ULNORTH |
| EASTDIFF | UREAST - ULEAST |
| URNORTH | Upper right corner point Northing (field 66) |
| ULNORTH | Upper left corner point Northing (field 55) |
| UREAST | Upper right corner point Easting (field 64) |
| ULEAST | Upper left corner point Easting (field 53) |

Field 113 (bytes 1062-1065) in Line fourteen contains the sun elevation in degrees for the scene center location at the scene center acquisition time.  This angle specifies the solar parallel of altitude on the celestial sphere as referenced from the celestial horizon of the scene center.

Field 115 (bytes 1086-1090) contains the sun azimuth (west) in degrees for the scene center location at the scene center acquisition time.  This angle specifies the vertical circle (West) on which the sun's location is measured from the principal vertical circle of the scene center.

## 2.2 SOFTWARE :

The cartographic software package used in processing the digital imagery is described in the following references:

General Cartographic Transformation Package (GCTP)

Software Reference

NOAA Technical Report NOS 124 CGS 9

General Cartographic Transformation Package GCTP, Version II

Atef A Elassal - February 1987

U.S.Dept. of Commerce

National Geodetic Information Center, NOAA

Rockville, MD 20852

USGS Map Projection Reference

Map Projections - A Working Manual

U.S. Geological Survey Professional Paper 1395

(Supersedes USGS Bulletin 1532)

John P. Snyder - 1987

USGS Map Sales

P.O.Box 25286

Denver, CO 80225

## APPENDIX-A :  Map Projections

This appendix contains the map projections used in EOSAT's products.  This list of map projections shows the name and the identifier used in Record 3.  Field 3 of the header file.

| Projection Name | Mnemonic |
| --- | --- |
| Universal Transverse Mercator | UTM |
| State Plane Coordinate System | SPCS |
| Albers Conical Equal Area | ACEA |
| Lambett's Conformal Conic | LCC |
| Mercator | MER |
| Polar Stereographic | PS |
| Polyconic | PC |
| Equidistant Conic (Type A & B) | EC |
| Transverse Mercator (Gauss-Krugger) | TM |
| Transverse Mercator | TM |
| Stereographic | SG |
| Lamberts Azimuthal Equal Area | LAEA |
| Azimuthal Equidistant | AE |
| Gnomonic | GNO |
| Orthographic | OG |
| General Vertical Near-Side Perspective | GVNP |
| Sinusoidal | SIN |
| Equirectangular (Plate Career) | ER |
| Miller Cylindrical | MC |
| Van Der Grintern I | VDG |
| Oblique Mercator (Type A & B) | OM |
| Space Oblique Mercator | SOM |

## APPENDIX- B-1 : Earth Ellipsoids

This appendix contains the earth ellipsoids used in products.

This list of ellipsoids shows the name and the identifier used in Record

- Field 3 of the header file.

| Ellipsoid Name | Semi-Major Axis (meters) | Semi-Minor Axis (meters) | Mnemonics |
| --- | --- | --- | --- |
| Clarke 1866 | 6378206.400000 | 6356583.800000 | CLARKE_1866 |
| Clarke 1880 | 6378249.145000 | 6356514.869550 | CLARKE_1880 |
| International 1967 | 6378157.500000 | 6356772.200000 | INTERNATL_1967 |
| International 1909 | 6378388.000000 | 6356911.646130 | INTERNATL_1909 |
| WGS 66 | 6378145.000000 | 6356759.769356 | WGS_66 |
| WGS 72 | 6378135.000000 | 6356750.519915 | WGS_72 |
| WGS 84 | 6378137.000000 | 6356752.314000 | WGS_84 |
| GRS 1980 | 6378137.000000 | 6356752.314140 | GRS_80 |
| Airy | 6377563.396000 | 6356256.910000 | AIRY |
| Modified Airy | 6377340.189000 | 6356034.448000 | MODIFIED_AIRY |
| Everest | 6377276.345200 | 6356075.41330 | EVEREST |
| Modified Everest | 6377304.063000 | 6356103.039000 | MODIFIED_EVEREST |
| Mercury 1960 | 6378166.000000 | 6356784.283666 | MERCURY_1960 |
| Modified Mercury 1968 | 6378150.000000 | 6356768.337303 | MOD_MERC_1968 |
| Bessel | 6377397.155000 | 6356078.962840 | BESSEL |
| Walbeck | 6376896.000000 | 6355834.846700 | WALBECK |
| Southeast Asia | 6378155.000000 | 6356773.320500 | SOUTHEAST_ASIA |
| Australian Natl. | 6378160.000000 | 6356774.719000 | AUSTRALIAN_NATL |
| Krassovsky | 6378245.000000 | 6356863.018800 | KRASSOVSKY |
| Hough | 6378270.000000 | 6356794.343479 | HOUGH |
| 6370997 Sphere | 6370997.000000 | 6370997.000000 | 6370997_M_SPHERE |

## APPENDIX- B-2: Ellipsoid and Datum Mnemonics

| Ellipsoid Name | Ellipsoid Mnemonic | Possible Datum Name | Datum Mnemonics |
| --- | --- | --- | --- |
| Clarke 1866 | CLARKE_1866 | Datum_North_American_Datum_1927 | NAS-E |
| Clarke 1880 | CLARKE_1880 | Datum_Adindan | ADI-M |
| International 1967 | INTERNATL_1967 | Datum_New_Zealand_Geodetic_Datum_1949 | GEO |
| International 1909/1924 | INTERNATL_1909 | Datum_European_Datum_1950 | EUR-M |
| WGS 66 | WGS_66 | WGS_66 | WGS_66 |
| WGS 72 | WGS_72 | WGS_72 | WGS_72 |
| WGS 84 | WGS_84 | WGS_84 | WGS_84 |
| GRS 1980 | GRS_80 | Datum_North_American_Datum_1983 | NAR-B |
| Airy | AIRY | Datum_OSGB_1936 | OGB_M |
| Modified Airy | MODIFIED_AIRY | Datum_TM65 | IRL |
| Everest | EVEREST | Datum_Kalianpur | IND-I |
| Modified Everest | MODIFIED_EVEREST | Datum_Kalianpur | IND-I |
| Mercury 1960 | MERCURY_1960 | NOT DEFINED |  |
| Modified Mercury 1968 | MOD_MERC_1968 | NOT DEFINED |  |
| Bessel | BESSEL | Datum_Tokyo | TOY-M |
| Walbeck | WALBECK | Datum_European_Datum_1950 | EUR-M |
| Southeast Asia | SOUTHEAST_ASIA | Datum_Southasia | SOA |
| Australian Natl. | AUSTRALIAN_NATL | Datum_Australian_Geodetic_datum_1984 | AUG |
| Krassovsky | KRASSOVSKY | Datum_Pulkovo_1942 | PUK |
| Hough | HOUGH | Datum_Wake-Eniwetok_1960 | ENW |
| 6370997 Sphere | 6370997_M_SPHERE | NOT DEFINED |  |

## APPENDIX – C : USGS    Projection Parameters

Fast Format Revision C Supports 17 USGS projections. For all projections except State Plane, USGS parameters 1 and 2 are semi major and minor axes of the requested earth ellipsoid.

*  Not every parameter will be used by the designated projection.

*  If a parameter is not used the field for the parameter will be initialized to Zero.

*  All latitude and longitude fields will be specified in Decimal Degree (floating point)

*  All other fields will be specified as double precision floating point values.

Please note that all co-ordinates for State Plane System contained in the Fast

Format is in map metres (not in feet).

C1(U) Universal Transverse Mercator ( UTM )

Parameter 3* 	UTM  Zone number ( Optional  )

C2(A) Albers Conical Equal Area  (  ACEA  )

Parameter 3 		Latitude of first Standard Parallel

Parameter 4		Latitude of second Standard Parallel

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C3(L) Lamberts Conformal Conic ( LCC )

Parameter 3 		Latitude of first Standard Parallel

Parameter 4		Latitude of second Standard Parallel

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C4(M) Mercator ( Mer )

Parameter 5		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C5(D)  Polar Stereographic ( PS )

Parameter 5		Longitude directed straight down below pole of map

Parameter 6 		Latitude of true scale

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C6(P)  Polyconic ( POL )

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	          	False Northing (in metres)

C7(T) Tranverse Mercator ( TM )

Parameter 3 		Scale Factor at central meridian

Parameter 5		Longitude of central meridian

Parameter 6		Latitude of projections's origin

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C8(H)  Stereographic ( SG )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C9(Z)  Lamberts Azimuthal Equal Area ( LAEA )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C10(E)  Azimuthal Equidistant ( AE )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C11(G) Gnomonic ( GNO )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C12(R) Orthographic ( OG)

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C13(N) General Vertical Near-Side Perspective ( GVNP )

Parameter 3		Height of perspective point above sphere

Parameter 5 		Longitude of centre of projection

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C14(I) Sinusoidal  ( SIN )

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	          	False Northing (in metres)

C15(C) Miller Cylinderical ( MC)

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C16(V)  Van Der Grinten ( VDG )

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C17(S) Space Oblique Mercator ( SOM )

Parameter 4                    Angle of azimuth east of north for central line

of projection

Parameter 9                    Longitude of the ascending Node

Parameter 11                  Longitude of descending Node

C18(K) Tranverse Mercator (Gauss-Krugger)( TM )

Parameter 3 		Scale Factor at central meridian

Parameter 5		Longitude of central meridian

Parameter 6		Latitude of projections's origin

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

## APPENDIX-D : Fast Format Header File Record Format Tables

The following tables are a description of the three records in the Header File.  Each record described below is separated by a blank typed line every eighty characters for case for reading.  A group of eighty characters can be thought of as a (printed) line.  See the accompanying text for more explanation of critical entries.

Administrative Record

| Line | Field | Start Byte | End Byte | Format | Description |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 2 3 4 5 6 7 8 | 1 13 24 35 52 71 79 80 | 12 23 34 51 70 78 79 80 | A12 A11 A11 A17 A19 A8 1X A1 | "PRODUCTbIDb=" Product order number in yydddnnn-cc format yyddd=First 1 to 5 Char nnn=8-10th char, of Unique ProductID. cc=Scene Number. "bLOCATIONb=" First scene location path/ row/fraction(shift %)/subscene(or quadrant) in ppp/rrrffss format In case of LISS4 Multi Spectral Mode Path=Strip Number,Row=Scene Number. "bACQUISITIONbDATEb=" First scene acquisition date in yyyyddmm format Blank fill Carriage return |
| 2 | 9 10 11 12 13 14 15 16 17 | 81 92 102 111 121 135 141 154 160 | 91 101 110 120 134 140 1453 159 160 | A11 A10 A9 A10 A14 A6 A13 F6.2 A1 | "SATELLITEb=" First scene satellite Name:IRS 1C,1D,P6 "bSENSORb=" First scene sensor Name: LISS3, PAN, WIFS, LISS4, AWIFS "bSENSORbMODEb=" First scene sensor Mode: For IRS-P6 PLD/SSD/SSN for LISS3,AWIFS PLD/SSD/SSN MN for LISS4 MONO mode PLD/SSD/SSN MX for LISS4 MX mode Blank fill for other satellites “bLOOKbANGLEb=”First scene off-nadir angle in degrees Carriage return |
| 3 | 18 19 20 21 22 23 24 | 161 184 195 212 231 239 240 | 183 194 211 230 238 239 240 | 23X A11 A17 A19 A8 1X A1 | Blank fill "bLOCATIONb=" Second scene location path/ row/fractions/subscene in ppp/rrrffss format "bACQUISITIONbDATEb=" Second scene acquisition date in yyyyddmm format Blank fill Carriage return |
| 4 | 25 26 27 28 29 30 31 32 33 | 241 252 262 271 281 295 301 314 320 | 251 261 270 280 294 30 313 319 320 | A11 A10 A9 A10 A14 A6 A13 F6.2 A1 | "SATELLITEb=" Second scene satellite Name:,1C,1D,P6 "bSENSORb=" Second scene sensor Name: PAN, WIFS,LISS4,AWIFS "bSENSORbMODEb=" Second scene sensor Mode "bLOOKbANGLEb=" Second scene off-nadir angle in deg. Carriage return |
| 5 | 34 35 36 37 38 39 40 | 321 344 355 372 391 399 400 | 343 354 371 390 398 399 400 | 23X A11 A17 A19 A8 1X A1 | Blankfill "bLOCATIONb=" Third scene location path/ row/fraction/subscene in ppp/rrrffss format "bACQUISITIONbDATEb=" Third scene acquisition date in yyyyddmm format Blank fill Carriage return |
| 6 | 41 42 43 44 45 46 47 48 49 | 401 412 422 431 441 455 461 474 480 | 411 421 430 440 454 460 473 479 480 | A11 A10 A9 A10 A14 A6 A13 F6.2 A1 | "SATELLITEb=" Third scene satellite Name: 1C,1D,P6 "bSENSORb=" Third scene sensor Name: LISS3, PAN, WIFS,LISS4,AWIFS "bSENSORbMODEb=" Third scene sensor Mode "bLOOKbANGLEb=" Third scene off-nadir angle in degree Carriage return |
| 7 | 50 51 52 53 54 55 56 | 481 504 515 532 551 559 560 | 503 514 531 550 558 559 560 | 23X A11 A17 A19 A8 1X A1 | Blank fill “Blocationb=” Fourth scene location path/ Row/fraction/subscene in Ppp/rrrffss format "bACQUISITIONbDATEb=" Fourth scene acquisition date in yyyyddmm format Blank fill Carriage return |
| 8 | 57 58 59 60 61 62 63 64 65 | 561 572 582 591 601 615 621 634 640 | 571 581 590 600 614 620 633 639 640 | A11 A10 A9 A10 A14 A6 A13 F6.2 A1 | "SATELLITEb=" Fourth scene satellite Name: 1C,1D,P6 "bSENSORb=" Fourth scene sensor Name: LISS3,PAN, WIFS, LISS4,AWIFS "bSENSORbMODEb=" Fourth scene sensor mode "bLOOKbANGLEb=" Fourth scene off-nadir angle In deg. Carriage return |
| 9 | 66 67 68 69 70 71 | 641 655 673 688 698 720 | 654 672 687 697 719 720 | A14 A10 A15 A10 22X A1 | "PRODUCTbTYPEb=" Product type: MAPbORIENT0dbbbbbb'. 'ORBITbORIENTEDbbbb' "bPRODUCTbSIZEb=" Product size:'FULLbSCENE', 'SUBSCENEbb'. 'MAPbSHEETb'.,'QUADRANT'. blank fill carriage return |
| 10 | 72 73 74 75 76 77 | 721 741 752 765 767 800 | 740 751 764 766 799 800 | A20 A11 A13 A2 33X A1 | "TYPEbOFbPROCESSINGb=" Type of processing used: 'SYSTEMATICb','PRECISIONbb', 'TERRAINbbbb','RADIOMETRIC", 'RAWbbbbbbbb' "bRESAMPLINGb=" Resampling algorithm used: 'CC','NN',’SI’,’KI’ Blank fill Carriage return |
| 11 | 78 79 80 81 82 83 84 85 86 87 88 89 | 801 820 822 823 825 843 848 865 870 871 876 880 | 819 821 822 824 842 847 864 869 870 875 879 880 | A19 I2 A1 I2 A18 I5 A17 I5 A1 I5 4X A1 | 'VOLUMEb#/#bINbSETb=" Tape volume number in tape set (for multi-volume image)"/" Number of volumes in tape set (for multi-volume image) “bPIXELSbPERLINEb=” Number of pixels per image Line “bLINESbPERb/BANDb=” Number of lines on this volume “/” Number of lines in the output Image Blank fill Carriage return |
| 12 | 90 91 92 93 94 95 96 97 98 | 881 895 900 918 920 936 941 954 960 | 894 899 917 919 935 940 953 959 960 | A14 I5 A18 I2 A16 I5 A13 F6.2 A1 | "STARTbLINEb#b=" First image line number on this vloume (for multi-volume image) "bBLOCKINGbFACTORb=" Tape blocking Factor "bRECORDbLENGTHb=" Length of physical file record in bytes "bPIXELbSIZEb=" Pixel size in meters Carriage return |
| 13 | 99 100 101 102 103 104 | 961 984 986 1012 1014 1040 | 983 985 1011 1013 1039 1040 | A23 I2 A26 I2 26X A1 | "OUTPUTbBITSbPERbPIXELb=" Output bits per pixel "bACQUIREDbBITSbPERbPIXELb=" Acquired bits per pixel Blank fills Carriage return |
| 14 | 105 106 107 108 109 110 | 1041 1056 1088 1103 1112 1120 | 1055 1087 1102 1111 1119 1120 | A15 A32 A14 A9 8X A1 | "BANDSbPRESENTb= Image bands present on this volume “PRODUCTbCODEb=” product code e.g. STPCD02AI ST : Two Char Product Type (e.g ST for STANDARD pathbased) P : 1 Char Projection Code (e.g. Polyconic) C : 1 Char Resampling Option (e.g. Cubic Convolution) D : 1 char Ellipsdoid Code ( e.g. Everest) 0 : Enhancement Code(Zero Always) I : Media Code(e.g. I for DAT, J for CDROM, Z for DISK) |
| 15 | 111 112 113 114 115 116 117 | 1121 1133 1145 1153 1171 1183 1200 | 1132 1144 1152 1170 1182 1199 1200 | A12 A12 8X A18 A12 17X A1 | “VERSION NO =” DPS software version Blank fill “ACQUISITIONbTIMEb=” time in HH:MM:SS:mmm Blank fill Carriage return |
| 16 | 118 119 120 121 122 123 124 | 1201 1221 1233 1236 1255 1265 1280 | 1220 1232 1235 1254 1264 1279 1280 | A20 A12 3X A19 A10 15X A1 | “GENERATINGbCOUNTRYb=” Generating Country Name Blank fill “GENERATINGbAGENCYb=” Generating Agency Name Blank Fill Carriage Return |
| 17 | 125 126 127 128 129 130 | 1281 1302 1310 1326 1333 1360 | 1301 1309 1325 1332 1359 1360 | A21 A8 A16 A7 27X A1 | “GENERATINGbFACILITYb=” facility Name “PRODUCTbENDIANb=” Endian in which product has been generated. e.g. BIG : For product generated with MOTOROLA Architecture(MSB First) LITTLE : For product generated with INTEL Architecture(LSB First) Blank fill Carriage return |
| 18 | 131 132 | 1361 1440 | 1439 1440 | 79X A1 | Blank fill Carriage return |
| 19 | 133 134 | 1441 1520 | 1519 1520 | 79X A1 | Blank fill Carriage return |
| 20 | 135 136 | 1521 1536 | 1535 1536 | 15X A | "REVbbbbbbbbbbbb" Format version code (A-Z). This document describes Version |

Radiometric Record

| Line | Field | Start Byte | End Byte | Format | Description |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 2 3 | 1 51 80 | 50 79 80 | A50 29X A1 | "BIASESbANDbGAINSbINbTHE bBANDbORDERbASbONbTHISbTAPE" Blank fill Carriage return |
| 2 | 4 5 6 7 8 | 81 105 106 130 160 | 104 105 129 159 160 | D24.15 1X D25.15 30X A1 | Bias for first Band on this tape Blank fill Gain for first Band on this tape Blank fill Carriage return |
| 3 | 9 10 11 12 13 | 161 185 186 210 240 | 184 185 209 239 240 | D24.15 1X D24.15 30X A1 | Bias for Second Band on this tape Blank fill Gain for second band on this tape Blank fill Carriage return |
| 4 | 14 15 16 17 18 | 241 265 266 290 320 | 264 265 289 319 320 | D24.15 1X D24.15 30X A1 | Bias for Third Band on this tape Blank fill Gain for Third band on this tape Blank fill Carriage return |
| 5 | 19 20 21 22 23 | 321 345 346 370 400 | 344 345 369 399 400 | D24.15 1X D24.15 30X A1 | Bias Fourth Band on this tape Blank fill Gain for Fourth Band on this tape Blank fill Carriage Return |
| 6 | 24 25 26 27 28 | 401 425 426 450 480 | 424 425 449 479 480 | D24.15 1X D24.15 30X A1 | * Bias for Fifth Band on this tape Blank fill Gain for Fifth Band on this tape Blank fill Carriage return |
| 7 | 29 30 31 32 33 | 481 505 506 530 560 | 504 505 529 559 560 | D24.15 1X D25.15 30X A1 | Bias for Sixth Band on this tape Blank fill Gain for Sixth Band on this tape Blank fill Carriage return |
| 8 | 34 35 36 37 38 | 561 585 586 610 640 | 584 585 609 639 640 | D24.15 1X D24.15 30X A1 | Bias for Seventh Band on this tape Blank fill Gain for Seventh Band on this tape Blank fill Carriage return |
| 9 | 39 40 41 42 43 | 641 665 666 690 720 | 664 665 689 719 720 | D24.15 1X D24.15 30X A1 | Bias for Eighth Band on this tape Blank fill Gain for Eighth Band on this tape Blank fill Carriage return |
| 10 | 44 45 | 721 800 | 799 800 | 79X A1 | Blank fill Carriage return |
| 11 | 46 47 48 49 | 801 520 852 880 | 819 851 879 880 | A19 8*I4 28X A1 | "SENSOR GAIN STATE=" bbbnbbbnbbbnbbbnbbbnbbbnbbbnbbbn Blank fill Carriage return |
| 12 | 50 51A 51B 51C | 881 895 903 960 | 894 902 959 960 | 14A A8 57X A1 | "SENSORbSTATEB=" Correction Alogrithm Used 1:ORIG or 2:CORLTN or 3:1DCC for LISS-3 GOOD or DEGRADED for PAN Default is GOOD. Blank fill Carriage return |
| 13 | 50 51 | 961 1040 | 1038 1040 | 79X A1 | Blank fill Carriage return |
| 14 | 52 53 | 1041 1120 | 1119 1120 | 79X A1 | Blank fill Carriage return |
| 15 | 54 55 | 1121 1200 | 1199 1200 | 79X A1 | Blank fill Carriage return |
| 16 | 56 57 | 1201 1280 | 1279 1280 | 79X A1 | Blank fill Carriage return |
| 17 | 58 59 | 1281 1360 | 1359 1360 | 79X A1 | Blank fill Carriage return |
| 18 | 60 61 | 1361 1440 | 1439 1440 | 79X A1 | Blank fill Carriage return |
| 19 | 62 63 | 1441 1520 | 1519 1520 | 79X A1 | Blank fill Carriage return |
| 20 | 64 65 | 1521 1536 | 1535 1536 | 15X A1 | Blank fill Carriage return |

* NOTE: - In IRS series only four bands are present so information

related to fifth to eighth band are filled with blank.

Geometric Record

| Line | Field | Start Byte | End Byte | Format | Description |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 2 3 4 5 6 7 8 | 1 15 32 36 48 66 74 80 | 14 31 35 47 65 73 79 80 | A14 A17 A4 A12 A18 A8 A6 A1 | "GEOMETRICbDATA" "bMAPbPROJECTIONb=" Map projection name (see Appendix A for list of mnemonies) "bELLIPSOIDb=" Earth Ellipsoid used (see Appendix B for list of mnemonies) "bDATUMb=" Datum name (see Appendix B for list of mnemonics) Carriage return |
| 2 | 9 10 11 12 13 14 15 | 81 109 110 134 135 159 160 | 108 109 133 134 158 159 160 | A28 1X D24.15 1X D24.15 1X A1 | "USGSbPROJECTIONbPARAMETERSb=" Blank fill USGS projection parameter #1:Semimajor axis Blank fill USGS projection parameter #1:Semiminor axis Blank fill Carriage return |
| 3 | 16 17 18 19 20 21 22 | 161 185 186 210 211 235 240 | 184 185 209 210 234 239 240 | D24.15 1X D24.15 1X D24.15 5x A1 | USGS projection parameter #3. Blank fill USGS projection parameter #4 Blank fill USGS projection parameter #5 Blank fill Carriage return |
| 4 | 23 24 25 26 27 28 29 | 241 265 266 290 291 315 320 | 264 265 289 290 314 319 320 | D24.15 1x D24.15 1x D24.15 5x A1 | USGS projection parameter #6 Blank fill USGS projection parameter #7 Blank fill USGS projection parameter #8 Blank fill Carriage return |
| 5 | 30 31 32 33 34 35 36 | 321 345 346 370 371 395 400 | 344 345 369 370 394 399 400 | D24.15 1x D24.15 1x D24.15 5x A1 | USGS projection parameter #9 Blank fill USGS projection parameter #10 Blank fill USGS projection parameter #11 Blank fill Carriage return |
| 6 | 37 38 39 40 41 42 43 | 401 425 426 450 451 475 480 | 424 425 449 450 474 479 480 | D24.15 1x D24.15 1x D24.15 5x A1 | USGS projection parameter #12 Blank fill USGS projection parameter #13 Blank fill USGS projection parameter #14 Blank fill Carriage return |
| 7 | 44 45 46 | 481 505 560 | 504 559 560 | D24.15 55X A1 | USGS projection parameter #15 Blank fill Carriage return |
| 8 | 47 48 49 50 51 52 53 54 55 56 57 | 561 565 566 579 580 592 593 606 607 620 640 | 564 565 578 579 591 592 605 606 619 639 640 | A4 1x A13 1x A12 1x F13.3 1x F13.3 20x A1 | "ULb=" Blank fill Geodetic Longitude of Upper Left corner of image. As per FIPS PUB 70, longitude will be expressed as FIBSPUB degrees, minutes, seconds. Example: 5 degrees, 15 minutes, 13.2 seconds west of the prime meridian will be "0051513.2000W" Blank fill Geodetic latitude of Upper Left corner of image. As per FIPS PUB 70latitude Will be expressed as Degrees, minutes, Seconds. Example: 9 degrees,4 minutes, 24.2334 seconds expressed as PUB 70 Seconds north of the Equator will be "090424.2334N" Blank fill Easting of Upper corner of image in projection units Blank fill Northing of Upper corner of image in projection units Blank fill Carriage return |
| 9 | 58 59 60 61 62 63 64 65 66 67 68 | 641 645 646 659 660 672 673 686 687 700 720 | 644 645 658 659 671 672 685 686 699 719 720 | A4 1x A13 1x A12 1x F13.3 1x F13.3 20X A1 | "URb=" Blank fill Geodetic Longitude of Upper Right corner of image Blank fill Geodetic Latitude of Upper Right corner of image Blank fill Easting of Upper Right corner Of image in projection units Blank fill Nothing of Upper Right corner Of image in projection units Blank fill Carriage return |
| 10 | 69 70 71 72 73 74 75 76 77 78 79 | 721 725 726 739 740 752 753 766 767 780 800 | 724 725 738 739 750 752 765 766 779 799 800 | A4 1x A13 1x A12 1x F13.3 1x F13.3 20X A1 | "LRb=" Blank fill Geodetic Longitude of Lower Right corner of image Blank fill Geodetic Latitude of Lower Right corner of image Blank fill Easting of Lower Right Corner Of image in projection units Blank fill Northing of Lower Right corner Of image in projection units Blank fill Carriage return |
| 11 | 80 81 82 83 84 85 86 87 88 89 90 | 801 805 806 819 820 832 833 846 847 860 880 | 804 805 818 819 831 832 845 846 859 879 880 | A4 1x A13 1x A12 1x F13.3 1x F13.3 20X A1 | "LLb" Blank fill Geodetic Longitude of Lower Corner of image Blank fill Geodetic Latitude of Lower Corner of image Blank fill Easting of Lower Left corner Of image in projection units Blank fill Northing of Lower Left corner of image in projection units Blank fill Carriage return |
| 12 | 91 92 93 94 95 96 97 98 99 100 101 102 103 104 105 | 881 889 890 903 904 916 917 930 931 944 945 950 951 956 960 | 888 889 902 903 915 916 929 930 943 944 949 950 955 959 960 | A8 1x A13 1x A12 1x F13.3 1x F13.3 1x I5 1x I5 4x A1 | "CENTERb=" Blank fill Scene centre geodetic longitude expressed in degrees, as above. This is the true center of the full scene product image was made, and does not product image. Blank fill Scene center geodetic latitude expressed in degrees, minutes seconds as above. This is the true centre of the full scene from which the product image was made and does not necessarily fall inside product image. Blank fill Scene center Easting in Projection units Blank fill Scene center Northing in Projection units Blank fill Scene center pixel number measured from the product upper left corner, rounded to nearest whole pixel (may be negative) Blank fill Scene center line number measured from the product upper left corner rounded to nearest whole pixel (may be negative) Blank fill Carriage return |
| 13 | 106 107 108 109 110 111 | 961 969 975 995 1001 1040 | 968 974 994 1000 1039 1040 | A8 I6 20A F6.2 39x A1 | "OFFSETb=" Horizontal offset of the true scene center in units of whole pixels. (may be negative) "bORIENTATIONbANGLEb=" Orientation angle in degrees (may be negative) Blank fill Carriage return |
| 14 | 112 113 114 115 116 117 118 119 | 1041 1062 1066 1086 1091 1102 1114 1120 | 1061 1065 1085 1090 1101 1113 1119 1120 | 21A F4.1 A20 F5.1 A11 F12.5 6X A1 | "SUNbELEVATIONbANGLEb=" Sun elevation angle in Degrees at scene center "bSUNbAZIMUTHbANGLEb=" Sun azimuth in degrees at scene center “bALTITUDEb=” Altitude in Meters. Blank fill Carriage return |
| 15 | 120 121 122 | 1121 1136 1150 1200 | 1135 1149 1199 1200 | A15 F14.6 50X A1 | “HEADINGbANGLEb= Satellite Heading Angle in degrees. Blank fill Carriage Return |
| 16 | 123 124 | 1201 1280 | 1279 1280 | 79X A1 | Blank fill Carriage return |
| 17 | 125 126 | 1281 1360 | 1359 1360 | 79X A1 | Blank fill Carriage Return |
| 18 | 127 128 | 1361 1440 | 1439 1440 | 79X A1 | Blank fill Carriage Return |
| 19 | 129 130 | 1441 1520 | 1519 1520 | 79X A1 | Blank fill Carriage Return |
| 20 | 131 132 | 1521 1536 | 1535 1536 | 79X A1 | Blank fill Carriage Return |

## APPENDIX-E : Fast Format Layout

Header File

< E O F >

< E O F >

< E O F >

< E O F >

< E O F >

# Text boxes

Administrative Record (1536 Bytes)

Geometric Record (1536 Bytes)

Radiometric Record (1536 Bytes)

Image Data for First Band

## Image Data for Second Band

### Image Data for nth Band

Where n = No. of Bands present

In the product