DOCUMENT CONTROL AND DATA SHEET

TABLE OF CONTENTS

1.0 INTRODUCTION	5

2.0 SUPER STRUCTURED DIGITAL DATA FORMAT	6

2.1 FILE ORGANIZATION	6

2.1.1 LOGICAL VOLUME	6

2.1.2 VOLUME DIRECTORY FILE	6

2.1.3 LEADER FILE	6

2.1.4 IMAGE FILE	6

2.1.5 TRAILER FILE	6

2.1.6 NULL VOLUME DIRECTORY FILE	6

2.2 FILES AND RECORDS IN IRS-1C/1D/P3/P6/DAT	7

2.3 FILE STRUCTURE/NOMENCLATURE	8

2.3.1 DIGITAL DATA FILE STRUCTURE	8

2.3.2 CDROM Products Naming Conventions	9

2.3.2 DISK Products Naming Conventions	10

2.4  RECORD STRUCTURE	11

2.4.1  VOLUME DIRECTORY	11

2.4.2  FILE DESCRIPTOR RECORD	16

2.4.3  LEADER FILE	18

2.4.4 IMAGE DATA FILE	41

2.4.5 TRAILER FILE	45

2.4.6  NULL FILE	46

APPENDIX – 1A: CLARIFICATION OF EXISTING FORMAT	52

APPENDIX – 1B: USGS Projection Parameters	53

APPENDIX  - 1C : Earth Ellipsoids	56

APPENDIX  - 1D : Ellipsoid and Datum Mnemonics	57

APPENDIX  - II: Super Structure format Layout	58

## 1.0 INTRODUCTION

IRS-1C/1D/P3/P6 Data products system generates digital video data in DATs, CD-ROM and DISK on the basis of user requests. Hence forth these products will be referred to as Digital Product in general.

Digital products are supplied in four formats such as  a)LGSOWG(Landsat Ground Station Operators Working Group) or  Super Structure Format , b) GeoTIFF, c) Fast Format and d) HDF. This document gives details of LGSOWG Format Only. Video data will be provided in BIL or BSQ formats.

Whereas in super structure format apart from the video data each digital product contains scene identification, location information, sensor, platform and processing related information.

The clarification related to various records of LGSOWG format is given in APPENDIX-1A.

Map projection parameters are given in APPENDIX-1B.

The superstructure layout in BIL and BSQ are shown in Figure-1 and APPENDIX-II.

Standard conventions used in the document is given in the Table number 1.0.

TABLE 1.0

Explanation for the notations used to describe the data type

Notation                    Explanation

B               :  Field coded in Binary

A               : Alphanumeric in ASCII

N               :  Numeric in ASCII

In              :  Integer numeric string with Length equal to n bytes.

Fw.d          :  Floating point numeric string with length w, with d decimal    digits.

NOTES:

1) Alpha-numeric information is left justified.

2) Numeric information is right justified.

## 2.0 SUPER STRUCTURED DIGITAL DATA FORMAT

## 2.1 FILE ORGANIZATION

The LGSOWG format contains basically five file as described below.

### 2.1.1 LOGICAL VOLUME

A logical volume is a logical collection of one or more files recorded consecutively.

All logical volumes have a volume directory as the first file and null volume directory as the last file. When a logical volume is split between physical volumes the volume directory is repeated at the start of the next physical tape with some updated information.

### 2.1.2 VOLUME DIRECTORY FILE

The volume directory file is the first file of every logical volume. It is composed of volume descriptor record, a number of file pointer records and a text record.

The volume descriptor record identifies the logical volume and the number of files it contains.

There is a file pointer record for each type of file in the logical volume, which indicates each file's class, format and attributes.

### 2.1.3 LEADER FILE

The leader file is composed of a file descriptor record and   three types of data records. The record types are header, ancillary and annotation.  Header contains information related to mission; sensor and processing parameters Ancillary records contain information related to ephemeries, attitude and Ground Control Points (GCPs) for image correction.

### 2.1.4 IMAGE FILE

Image file consists of file descriptor record and image data records. Image data record contain the video data in Band Interleaved by Line (BIL) format or Band Sequential Format (BSQ), and in addition, it also contains prefix and suffix information.

### 2.1.5 TRAILER FILE

The trailer file follows the image data file. This is composed of a file descriptor record and one trailer record for each band.

### 2.1.6 NULL VOLUME DIRECTORY FILE

The file, which ends a logical volume, is the null volume directory file. The file is referred as 'null' because it defines a non-existent (empty) logical volume. This file contains a volume descriptor record.

## 2.2 FILES AND RECORDS IN IRS-1C/1D/P3/P6/DAT

| File Seq. No. | Record Type and length | Description of file contents |
| --- | --- | --- |
| File 0 | Variable no of Records each of 360 bytes. | Volume Directory file (Volume descriptor, File Pointers and text record). |
| File 1 | * Variable no of Records each of 6120 bytes | Leader file (Descriptor, Header, ancillary, Calibration, histogram, map projection, GCP, annotation, Boundary, and Boundary annotation Record. CLASS LEAD |
| File2 | * VariableNo.of records * Variable record length | Image Data file CLASS IMGY |
| File 3 | Variable no of Records each of 360 bytes | Trailer file (Description and trailer records) CLASS TRAI |
| NULL | One Record of 360 bytes | Null file (End of logical volume will be overwritten to add another logical volume.) |

*  Number. of records and record length will vary as per the product type or number.  of bands or sensor.

## 2.3 FILE STRUCTURE/NOMENCLATURE

### 2.3.1 DIGITAL DATA FILE STRUCTURE

| Volume Directory | i) Volume Descriptor ii) File Pointer for file-1 iii) File Pointer for file-2 iv) File pointer for file-3 v) Text Record | Volume Direc- Tory file | Identification of logical Volume and file pointer record corresponding to each file of logical volume. Specific file format record length, number of records etc The text record gives information about physical tape, environment in which the tape has been created. |
| --- | --- | --- | --- |
| 1. . | i) Leader file Descriptor ii) Header Record iii) Ancillary Records iv) Annotation Record v) Boundary Records and Boundary annotation record | Leader file (LEAD) | Gives the mode of reading file and contains key data field location. Information related to mission, sensor, processing parameters. Contains information about ephemeris, attitude, calibration histogram, map projection and GCP's Contains information about annotation and tick marks. These records are dummy. |
| 2. | i) Image file descriptor ii) Image data Records | Image data file (IMGY) | Gives the mode of reading the file and contains key data field locations. Contains RAW/PROCESSED/RADIOMETRIC Corrected Data |
| 3. | i) Trailer file descriptor ii) Trailer records | Trailer file TRAI | Gives the mode of reading the file and contains key data field locations. These contain information about cloud coverage and parity errors. |
| NULL VOLUME | i) NULL VOLUME Descriptor Record | Null Volume file | Last file of the logical volume. The purpose of this is to mark the end of logical volume. |

### 2.3.2 CDROM Products Naming Conventions

In case of CDROM product a typical CD will contain following files.

- CDINFO – a file describing the Satellite name, Product Code, Path, Row, Date Of Pass, Sensor, Volume number etc. It is basically gives the information about the contents of CD. Typical content of a CDINFO file for P6 will look like this.

PRODUCT 1 :

Product number			: JobId  	               (Twelve Character)

Satellite ID			: P6                  	   (Two Character)

Sensor				: L-3                		   (Three Character)

Path-Row				: 096-055         	   (Seven Character)

Date& time of Acquisition 	: 28-MAR-02 05:50:39   Eighteen Character)

Product Code			: STPCD027J 		   (Nine Character)

Orbit Number			: 1

Image Layout			:BSQ

Number of Bands			: 4

Bands Present in Product		: 2 3 4 5

Bands in this volume       		: 2 3 4 5

File Header			: 540

Line Header (Prefix Bytes )	: 32

Line Trailer (Suffix Bytes )	: 0

Scan Lines				: 5545

Pixels				: 5918

Bytes Per Pixel			: 1

Image Record Length (Bytes)	: 5950

No of Volume			: 1/1                 	   (3 Chracter-CurVol/NoOfPhyVol)

- PRODUCT1- a directory containing following files.

  - VOLUME.SensorCode/DAT – the Volume Directory File.

  - LEADER.SensorCode/DAT  -  the Leader File.

  - IMAGERYb.SensorCode/DAT- the Imagery File.

  - TRAILER.SensorCode/DAT – the Trailer File.

  - NULL.SensorCode/DAT   - the Null Volume File.

Where b=Band number. In case of PAN ‘b’ will not be present. and SensorCode=Three Character Sensor Code , shown in Table 2.3.1 below.

| Sr. No. | Sensor Name | Sensor Code (Three Character) | Possible values for ‘b’ used in Imagery File. |
| --- | --- | --- | --- |
| 1 | LISS-3 | L-3(for 1C/1D/P6) | 2,3,4,5 |
| 2 | LISS-4 | L-4 | 2,3,4 |
| 3 | AWiFS | AWF | 2,3,4,5 |
| 4 | PAN | PAN (for 1C/1D) | NIL |
| 5 | WiFS | WIF (for 1C/1D) | 3,4 |

Table 2.3.1 Sensor Code and Band Combination

NOTE : The default file name extension is .SensorCode. The alternative extension available is .DAT. The extension based on sensor code and DAT is configurable as per user requirement.

###### Multi Volume CD Products

In case of multi volume CD-ROM products the file structure will be similar to single volume except the entry against No of volume field in CDINFO file. The Number of volume field will have entry like

CurrentPhysicalVolume/TotalNoOfPhysicalVolume.

e.g. For a two volume CD Product CDINFO file will have following entries  entry

No of  Volume  : 1/2          (CDINFO of volume1)

No of Volume   : 2/2          (CDINFO of volume2)

###### More than one Products in a single CD

In case of more than one products to be written into a single CD there will be a separate directory entry for each product to distinguish each. The name of the directory will be 12 character Job id. The contents within individual directories will be exactly similar to single product CD.

e.g. consider two products with 12 character JobId1 and JobId2. The CDROM will contain two directories named JobId1 and JobId2. The underlying contents of these directories will be exactly similar to single product in single CD.

NOTE : The directory structure  for CDROM products will be same for all formats (LGSOWG, Fast Format, GeoTIFF, HDF). CDINFO file contents will also be similar for all formats. Only the contents of the PRODUCT1 directory will vary from format to format. The structure for multi volume CD and single CD containing multiple products also will be same for all CDROM products irrespective of formats.

### 2.3.2 DISK Products Naming Conventions

The disk products will be generated on the disk in specified directory, configured by DISK_FILE_PATH in DPS Scheduler setup. Following files will be generated in disk file path.

JobId.vol – the Volume Directory File.

JobId.led -  the Leader File

JobId/JobId_bn.img- the Imagery File.

JobId.trl – the Trailer file

JobId.nul- the Null Volume File.

Where JobId= 12 character uniquerequest or Job Identification code.

bn = Band Number . Not relevant for PAN. So in case of PAN JobId.img will be created.

## 2.4  RECORD STRUCTURE

### 2.4.1  VOLUME DIRECTORY

- Volume Descriptor Record

ii)    File Pointer Records (number of records will depend on the number of files in the

product).

iii)   Text Record

The table in the next page describes the Volume Directory in detail.

TABLE 2.4.1.1

VOLUME DESCRIPTOR RECORD : (DEFINITIONS /CONTENTS)

(360 Bytes)

| FIELD NO. | BYTE NO | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | The record number of this record within the file (1) |
| 2 | 5-8 | B | Record type and subtype octal codes ("300 300 022 022") |
| 3 | 9-12 | B | Length of this record (360) |
| 4 | 13-14 | A | ASCII/EBCDIC Flag (Ab) - A2 |
| 5 | 15-16 | A | Product Endian e.g. MM (Motorola-Big Endian) or II (Intel –Little Endian) |
| 6 | 17-28 | A | Super structure format control document number - A12 |
| 7 | 29-30 | N | Super structure control document revision number - I2 |
| 8 | 31-32 | A | Super structure control document revision letter - A2 |
| 9 | 33-44 | A | Software release number A12 (ex. IRS P6DPSV1R2) |
| 10 | 45-60 | A | Tape ID for physical volume containing this volume descriptor - A16 (D 010008600 401-01) UXXXXXXXXXXXX-NN (U = C/Z/D)Z=DISK U = Output Media Symbol; C: CDROM,, D: DAT, U: Other Media XXXXXXXXXXXX = Unique identification of the product NN = Current physical volume in volume set |
| 11 | 61-76 | A | Logical volume ID - A16 (P6-MS-BSQ-L-3-01) SS-NN-MMM-LLL-KK SS = Satellite Id. (e.g. 1C/1D/P6) NN = Mode of data acquisition (PA for panchromatic, MS for multi spectral mode) MMM= Interleaving indicator (BIL or BSQ) LLL=Sensor Identification (L-3, WIF, PAN,L4M,L4X,AWF) KK = Present logical volume no in volume set |
| 12 | 77-92 | A | Volume set ID - A16 (P6-MS-BSQ-L-3-01) SS-NN-MMM-LLL-KK KK = Total no. of logical volume in volume set rest defined in field 11. |
| 13 | 93-94 | N | Number of physical volume in the Volume set - I2 |
| 14 | 95-96 | N | Physical volume number, start of logical volume - I2 |
| 15 | 97-98 | N | Physical volume number, end of logical volume - I2 |
| 16 | 99-100 | N | Physical volume number containing this volume descriptor - I2 |
| 17 | 101-104 | N | First file number reference in this physical volume - I4 |
| 18 | 105-108 | N | Logical volume number within volume set - I4 |
| 19 | 109-112 | N | Logical volume number within this physical volume - I4 |
| 20 | 113-120 | A | Logical volume creation date (YYYYMMDD) - A8 |
| 21 | 121-128 | A | Logical volume creation time (HHMMSS)- A8 |
| 22 | 129-140 | A | Logical volume generating country - A12 (INDIA) |
| 23 | 141-148 | A | Logical volume generating agency - A8 |
| 24 | 149-160 | A | Logical volume creation facility - A12 |
| 25 | 161-164 | N* | Number of pointer records in volume directory (bbbN) - I4 |
| 26 | 165-168 | N* | Total Number of records in volume directory (bbbN) - I4 |
| 27 | 169-360 | - | Spares |

* These fields will have different contents for different products.

TABLE  2.4.1.2

FILE POINTER RECORDS : DEFINITIONS/CONTENTS ( 360 BYTES )

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | The record number of this record within the volume directory file (2,3 or 4) |
| 2 | 5-8 | B | Record type and subtype octal codes ("333 300 022 022") |
| 3 | 9-12 | B | Length of this record (360) |
| 4 | 13-14 | A | ASCII/EBCDIC flag (Ab) - A2 |
| 5 | 15-16 | - | Spares |
| 6 | 17-20 | N | Reference file number (bbb1, bbb2, or bbb3) - I4 |
| 7 | 21-36 | A | Referenced file name - A16 |
| 8 | 37-64 | A | Referenced file class (LEADERbFILEb,IMAGERYbFILE or TRAILERbFILE : Plus 16 blanks) - A28 |
| 9 | 65-68 | A | Reference file class code (LEAD, IMGY, TRAI) - A4 |
| 10 | 69-96 | A | Reference file data type MIXED BINARY AND ASCII (MBAA) or BINARY ONLY (BINO)- A28 |
| 11 | 97-100 | A | Referenced file data type code (MBAA or BINO) - A4 |
| 12 | 101-108 | N | Number of records in referenced file - I8 |
| 13 | 109-116 | N | Referenced file first record length - I8 |
| 14 | 117-124 | N | Referenced file maximum record length -I8 |
| 15 | 125-136 | A | Referenced file record length type - A12 |
| 16 | 137-140 | A | Referenced file record length type code - A4 |
| 17 | 141-142 | A | Referenced file physical volume, start of file - I2 |
| 18 | 143-144 | N | Referenced file physical volume, end of file - I2 |
| 19 | 145-152 | N | Referenced file, 1st record number in this physical volume - I8 |
| 20 | 153-160 | N | Referenced file, number of records in this physical volume - I8 |
| 21 | 161-360 | - | Spares |

TABLE - 2.4.1.3

TEXT RECORD: DEFINITIONS/CONTENTS (360 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Sequence Number of this record |
| 2 | 5-8 | B | Record type and subtype octal codes ("022 077 022 022") |
| 3 | 9-12 | B | Length of this record (360) |
| 4 | 13-14 | A | ASCII/EBCDIC Flag (Ab) - A2 |
| 5 | 15-16 | A | Continuation Flag (NO) - A2 |
| 6 | 17-32 | A | Product type (RAW, STEREO, PATH BASED, SPECIAL, GEOCODED, GEOR EFERENCED, RADIOMETRIC,ORTHO,PRECISION) - A16 |
| 7 | 33-48 | A | Date of product creation (DD-MM-YY)-A16 |
| 8 | 49-64 | A | Time of product creation (HH:MM:SS)-A16 |
| 9 | 65-80 | A | Physical tape ID (16 character long string as `name' to physical tape)- A16(+) |
| 10 | 81-112 | A | Scene ID - A32 (*) |
| 11 | 113-172 | A | State & District name - A60 |
| 12 | 173-180 | A | Map Sheet Number - A8 |
| 13 | 181-199 | A | Spares |
| 14 | 200-208 | A | Product Code - A9 (ST000017I) |
| 15 | 209-360 | A | Spares |

(*)  Scene ID coded as follows : (06-JAN-02 05:50:52 L-3 ST00B 2345F)

1.   1:8         DD-MMM-YY (Date of Pass)

2.    9:10      Blank

3.   11:18     HH:MM:SS (Time of acquisition in UT)

4.   19:21     Sensor ID (L-3,P-(A,B,C,D), WIF,AWF,L4M,L4X)

5.   22:22     Sub scene ID (0-9) ,A,B,C,D and F (for full scene )

6.   23:24     Product type code (e.g. ST/TR/QU/GR/G3/J3/G4/J4/J5/SR)

7.   25:26      % shift along   track

8.   27:27     'B'

9.   28:31     Band numbers

10.  32:32     Flag for full = 'F' or Quad='Q'

(+) Refer table No.2.4.1.1 (field No.10)

Note: YY in the Date of Pass field location  No. 7 & 8 is to be interpreted as follows..

99    ( 1999

00    ( 2000

01    ( 2001

### 2.4.2  FILE DESCRIPTOR RECORD

1.   	Fixed part of the file Descriptor record

TABLE 2.4.2.1

FIXED PART OF THE FILE DESCRIPTION RECORDS

DEFINITIONS/CONTENTS (180 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Number of this record within the file (1) |
| 2 | 5-8 | B | Record type and subtype octal codes ("077 300 022 022") |
| 3 | 9-12 | B | Length of this record |
| 4 | 13-14 | A | ASCII/EBCDIC Flag - A2 |
| 5 | 15-16 | - | Spares |
| 6 | 17-28 | A | Superstructure format control document number - A12 |
| 7 | 29-30 | N | Superstructure control document revision number - I2 |
| 8 | 31-32 | N | Superstructure control document revision letter - A2 |
| 9 | 33-44 | A | Software release number - A12 |
| 10 | 45-48 | N | Sequence number of this file within the logical volume (excluding volume directory) (1 or 2 or 3. etc) - I4 |
| 11 | 49-64 | A | File name (unique identification of the present file) |
| 12 | 65-68 | A | Record sequence and location type flag (Indicates whether other records in the file have sequence number or not) |
| 13 | 69-76 | N | Location of the start of the sequence number field (bbbbbbb4)-I8 |
| 14 | 77-80 | N | Length in bytes of the record sequence number field (bbb4) - I4 |
| 15 | 81-84 | A | Record code and location type flag (indicates whether other records in the file have a record type code or not and their location is fixed or not) |
| 16 | 85-92 | N | Location of the start of the record type code field (bbbbbbb5) - I8 |
| 17 | 93-96 | N | Length in bytes of the record type code field (bbb4) - I4 |
| 18 | 97-100 | A | Record length and location type flag (Indicates whether other records in this file have its record length recorded within the record or not and location is fixed or not: -FLGT (Fixed in IRS- format) - A4 |
| 19. | 101-108 | N | Location of the start of the record length field (bbbbbbb9) - I8 |
| 20. | 109-112 | N | Length in bytes of the record length field (bbb4) - I4 |
| 21. | 113 | A | Flag indicating that the data interpretation information is included with the file descriptor record - A1 |
| 22. | 114 | A | Flag indicating that the data interpretation information is included within the file in records other than the files descriptor record - A1 |
| 23. | 115 | A | Flag indicating that the data display information is included with the file description record - A1 |
| 24. | 116 | A | Flag indicating that the data display information is included within the file in records other than the file descriptor record - A1 |
| 25. | 117-180 | - | Spares |

### 2.4.3  LEADER FILE

1.  File Descriptor Record

2.  Header Record

3.  Ephemeris/Attitude Record

&  4.  Calibration Records

5.  Map Projection Record

6.  Histogram Records

7.  GCPs Record

8.  Annotation Record

*   9.  Line & Pixel look up table

$  10. Attitude Rate Record

$  11. Boundary Records

$  12. Boundary annotation Record

$  These records are dummy and not valid for P6.

&  Valid for Raw or Radiometrically corrected products. Other products will contain dummy record.

* Valid for Basic Stereo products only. Other products will contain dummy record.

TABLE 2.4.3.1

LEADER FILE DESCRIPTOR RECORD :

DEFINITIONS/CONTENTS (6120 Bytes)

| FIELD NO | BYTE NO | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-180 | - | See 2.4.2.1 (Fixed part of the file descriptor) |
| 2 | 181-186 | N | Number of header records (bbbbb1) - I6 |
| 3 | 187-192 | N | Header record length (bb6120) – I6 |
| 4 | 193-198 | N | Number of ancillary `Ephemeries/attitudes' record - I6 |
| 5 | 199-204 | N | Length of this record - I6 |
| 6 | 205-210 | N | Number of `Calibration'records - I6 |
| 7 | 211-216 | N | Length of these records - I6 |
| 8 | 217-222 | N | Number of ancillary `Histogram record'-I6 |
| 9 | 223-228 | N | Length of these records - I6 |
| 10 | 229-234 | N | Number of `MAP PROJECTION' records -I6 |
| 11 | 235-240 | N | Length of these records - I6 |
| 12 | 241-246 | N | Number of `GCP'records - I6 |
| 13 | 247-252 | N | Length of these records - I6 |
| 14 | 253-258 | N | Number of annotation Records I6 |
| 15 | 259-264 | N | Length of these records - I6 |
| 16 | 265-270 | N | Line & pixel lookup table records- I6 |
| 17 | 271-276 | N | Length of these records I6 |
| 18 | 277-282 | N | Number of Attitude Rate Records - I6 |
| 19 | 283-288 | N | Length of these records - I6 |
| 20 | 289-294 | N | Number of boundary records -I6 |
| 21 | 295-300 | N | Length of these records -I6 |
| 22 | 301-306 | N | Number of boundary annotation records -I6 |
| 23 | 307-312 | N | Length of these records -I6 The location of the below mentioned fields is given in 16 bytes, coded as follows 6 bytes - the record number of the record containing the field 6 bytes - byte number of the 1st byte of this field 3 bytes - length of these fields in bytes 1 bytes - Code for the type of data in the field (A=alphanumeric, B=binary, N=numeric) |
| 24 | 313-324 |  | Spares |
| 25 | 325-340 | A | Scene identification field locator - A16 |
| 26 | 341-356 | A | Mission identification field locator -A16 |
| 27 | 357-372 | A | Sensor identification field locator - A16 |
| 28 | 373-388 | A | Exposure date & time locator - A16 |
| 29 | 389-404 | A | Geographic field reference locator - A16 |
| 30 | 405-420 | A | Image processing performed field locator - A16 |
| 31 | 421-436 | A | Imagery format indicator locator (Interleaving) - A16 |
| 32 | 437-452 | A | Band indicator locator – A16 |
| 33 | 453-6120 | - | Spares |

TABLE 2.4.3.2

HEADER RECORD : DEFINITION/CONTENTS - (6120 Bytes)

(For IRS-P6)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("022 022 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Header Record sequence number -I4 |
| 5 | 17-20 | - | Blanks |
| 6 | 21-28 | N | Path Number (bbbbbPPP)-I8 |
| 7 | 29-36 | N | Row Number (bbbbbRRR)-I8 |
| 8 | 37-68 | A | Scene Identification-A32 + |
| 9 | 69-100 |  | Spares |
| 10 | 101-116 | N | Scene Centre Geographic location (lat) (Deg.) - F16.7 |
| 11 | 117-132 | N | Scene Centre Geographic location (long) (Deg.) F16.7 |
| 12 | 133-140 | N | Scene centre location within image (line no.) -I8 |
| 13 | 141-148 | N | Scene centre location within image (pixel no) - I8 |
| 14 | 149-164 | N | Left top corner geographic location of scene (lat) (Deg.) - F16.7 |
| 15 | 165-180 | N | Left top corner geographic location of scene (long) (Deg.) - F16.7 |
| 16 | 181-188 | N | Left Top corner location in scene (line no.) - I8 |
| 17 | 189-196 | N | Left top corner location in scene (pixel no.) - I8 |
| 18 | 197-212 | N | Right top corner geographic location (lat)-F16.7 |
| 19 | 213-228 | N | Right Top corner geographic location (long) – F16.7 |
| 20 | 229-236 | N | Right top corner location in scene (line no ) - I8 |
| 21 | 237-244 | N | Right top corner location in scene (pixel no)-I8 |
| 22 | 245-260 | N | Left bottom corner geographic location of scene (lat.)-F16.7 |
| 23 | 261-276 | N | Left bottom corner geographic location of scene (long)- F16.7 |
| 24 | 277-284 | N | Left bottom corner location in scene (line no)-I8 |
| 25 | 285-292 | N | Left bottom corner location in scene (pixel no)-I8 |
| 26 | 293-308 | N | Right bottom corner geographic location of scene (lat)-F16.7 |
| 27 | 309-324 | N | Right bottom corner geographic location of scene (long)-F16.7 |
| 28 | 325-332 | N | Right Bottom corner location in scene (line no) -I8 |
| 29 | 333-340 | N | Right Bottom corner location in scene (pixel no) -I8 |
| 30 | 341-348 | N | Input nominal scene data (pixels)-I8 |
| 31 | 349-356 | N | Input nominal scene data (lines)-I8 |
| 32 | 357-364 | N | Input nominal pixel size at nadir - (meters) - F8.3 |
| 33 | 365-372 | N | Input nominal line spacing at nadir - (meters) – F8.3 |
| 34 | 373-388 | N | Input viewing angle (Deg.) - F16.7 |
| 35 | 389-396 | N | Input nominal pixels for SWIR band-I8 |
| 36 | 397-404 | N | Input nominal scans for SWIR band-I8 |
| 37 | 405-412 | N | Input nominal pixel size for SWIR band F8.3 |
| 38 | 413-420 | N | Input nominal line spacing for SWIRband I8 |
| 39 | 421-436 | N | Nominal orbit inclination (Deg.) - F16.7 |
| 40 | 437-452 | N | Nominal altitude (meters) - F16.7 |
| 41 | 453-468 | N | Longitude of ascending node, F16.7 |
| 41A | 469-470 | N | Endian Flag (0:for Big Endian, 1: Little Endian) |
| 41B | 471-472 | N | Shift percentage( 0 -99) I2, for shift along track products, I2 |
| 41C | 473-474 | N | Quadrant Number (Valid for Quadrant products only), I2 |
| 41D | 475-482 | A | CCD1CorrFlag |
| 41E | 483-501 | - | Spares |
| 42 | 502-517 | N | Satellite heading angle (Deg.) - F16.7 |
| 43 | 518-525 | N | Orbit Number, I8 |
| 44 | 526-541 | N | Instantaneous Cross track FOV in radians -F16.7 |
| 45 | 542-573 | - | Spares |
| 46 | 574-589 | N | Sun angle (Azimuth) (Deg.) – F16.7 |
| 47 | 590-605 | N | Sun angle (elevation) (Deg.) F16.7 |
| 48 | 606-621 | N | Predicated scene center latitude (deg.) F16.7 |
| 49 | 622-637 | N | Predicated scene centre longitude (deg.) F16.7 |
| 50 | 638-653 | N | Observed scene center latitude (deg.) F16.7 |
| 51 | 654-669 | N | Observed scene center longitude (deg.) F16.7 |
| # 52a | 670-679 | N | Roll BIAS F10.5 |
| # 52b | 680-689 | N | Pitch BIAS F10.5 |
| # 52c | 690-699 | N | Yaw BIAS F10.5 |
| # 52d | 700-703 | A | Pass Type PLD- Payload Pass,SSD-SSR Day Pass(Solid State Recorder),SSN-SSR Night Pass |
| # 52e | 704-797 | - | Spares |
| IMAGING PARAMETERS |
| 53 | 798-829 | A | Input scene start time (HH:MM:SS: mmm) |
| 54 | 830-845 | A | Mission identification-A16 |
| 55 | 846-877 | A | Sensor identification – A32 |
| 56 | 878-893 | A | Spectral mode – A16 |
| 57 | 894-913 |  | Spares |
| 58 | 914-929 | N | Day number within cycle-I16 |
| 59 | 930-937 | N | Payload tilt step number – I8 |
| 60 | 938-945 | N | Payload tilt per step in (Deg) – F8.3 |
| 61 | 946-961 | N | LISS-3 scene centre lat. Corresponding to PAN – F 16.7 |
| 62 | 962-977 | N | LISS-3 scene centre long. Corresponding to PAN – F 16.7 |
| 63 | 978-985 | N | LISS-3 Path no. Corresponding to PAN- I8 |
| 64 | 986-993 | N | LISS-3 Row no. Corresponding to PAN- I8 |
| 65 | 994-1009 | N | Integration Time for SWIR band – F 16.7 |
| 66 | 1010-1025 | N | Integration Time (in milli sec) – F 16.7 |
| # 67a | 1026-1061 | A | Start time for LISS-4 “nb” A12 |
| # 67b | 1062-1076 | N | Start pixel number for LISS-4 “nb” I5 |
| # 67c | 1077-1088 | - | Spares |
| 68 | 1089-1104 | N | On board gain number “nb” I4 |
| 69 | 1105-1112 | - | Spares |
| 70 | 1113-1120 | N | Number of spectral bands-I8 |
| 71 | 1121-1152 | N | Lower and upper limit of wavelength range in nanometers range in nanometers 2”nb” F4.2 where nb = no. of bands in the sensor. |
| 72 | 1153-1216 | N | CCD temp for all the CCD arrays present in sensor “nb” F8.4 (in degree Celsius) |
| 73 | 1217-1280 | - | Minimum (LMIN) & Maximum (LMAX) radiance for number of bands present in the product 2”nb” F8.5 (mw/sq. cm / str / micromet) |
| Conversion formula for Digital Count to radiance is as follows. Lrad = (DN/MaxGray)*(Lmax – Lmin) + Lmin. Lrad : Radiance for a given DN value. DN : Digital Count MaxGray : IRS-1C/1D : 63 for PAN & 127 for WiFS & LISS-3 for Raw Products only. 255 for Corrected products. For IRS-P6 : 127 for LISS-4 and LISS-3, 1023 for AWiFS for raw products only. 255 for LISS-3&4, 1023 for AWiFs for corrected products Lmin/Lmax: Minimum/Maximum radiance value for a given band. |
| IMAGE DATA PARAMETERS |
| 74 | 1281-1296 | N | Number of image pixels per line-I16 |
| 75 | 1297-1312 | N | Number of image data lines-I16 |
| 76 | 1313-1320 | N | Processed pixel spacing F8.3 |
| 77 | 1321-1328 | N | Processed line spacing F8.3 |
| 78 | 1329-1344 | A | Interleaving indicator-A16 |
| 79 | 1345-1360 | N | Spectral bands indicator – 4I4 |
| 80 | 1361-1368 | N | Processed pixel spacing for SWIR band F8.3 |
| 81 | 1369-1376 | N | Processed line spacing for SWIR band-F8.3 |
| 82 | 1377-1392 | N | Number of Image pixels per line for SWIR band – I16 |
| 83 | 1393-1408 | N | Number of Image data line for SWIRband – I16 |
| 84 | 1409-1440 |  | Spares |
| 85 | 1441-1456 | A | Preprocessing level identification-A16 LEVEL-0 : for RAW Products LEVEL-1 : for RAD Products (Radiometric Correction only) LEVEL-2 : for Radiometric Correction + Systematic Geometric Correction LEVEL-3 : Precision Corrected |
| 86 | 1457-1464 | A | Radiometric calibration designator-A8 DONE : for Radiometrically corrected products NOT DONE : for RAW products. |
| 87 | 1465-1472 | A | Resampling designator –I8 |
| 88 | 1473-1632 | - | Spares |
| 89 | 1633-1648 | N | Number of lines losses “nb”I4 |
| 90 | 1649-1664 | N | Number of dead detectors “nb”I4 |
| 91 | 1665-1669 | A | Multi Scene/Sensor flag (TRUE or FALSE) – A5 |
| 92 | 1670-1675 | N | No. of Mosaicked or merged scenes I6 |
| 93 | 1676-1707 | A | Second scene identification A32 |
| 94 | 1708-1713 | A | Second scene satellite identification A6 |
| 95 | 1714-1721 | N | Second scene input nominal resolution (meters) F8.3 |
| 96 | 1722-1737 | N | Second scene sun elevation angle (deg.) – F16.7 |
| 97 | 1738-1753 | N | Second scene sun azimuth angle (deg.) – F16.7 |
| 98 | 1754-1769 | N | Observed scene centre latitude (deg.) – F16.7 |
| 99 | 1770-1785 | N | Observed scene centre longitude (deg.) – F16.7 |
| 100 | 1786-1801 | N | Second scene heading angle (deg.) – F16.7 |
| 101 | 1802-1817 | N | Predicted second scene centre latitude (deg.) – F16.7 |
| 102 | 1818-1833 | N | Predicted Second Scene Centre Longitude (deg.) – F16.7 |
| 103 | 1834-3097 | N | Repetition of field no. 93,94,95,96,97,98,99,100,101,102 for remaining number of scenes. ( 8 times ) |
| # 104 | 3098-3098 | A | Source for orbit value flag– A1 0=Regular State Vec, 1=SANGAM processed Ground mode 2=SANGAM processed Onboard mode |
| # 105 | 3099-3099 | A | Source for attitude value flag– A1 0=Ground Attitude Determination not possible 1=ADAGE determined Q’s(ES+GYRO) 2=ADJUST determined Q’s(defau)(STAR SEN) 3=AOCE determined Q’s |
| # 106 | 3100-3100 | A | Yaw steering flag – A1 0=Yaw steering not done 1=Yaw steering done |
| # 107 | 3101-3124 | N | Stagger Value “nb” F6.3, Odd and Even detector Stagger Factor(no of lines) for L4 |
| # 108 | 3125-3125 | A | ADIF regeneration flag 1 to 9 (counter for Regenerated ADIF), 0=for Original ADIF |
| # 109 | 3126-3137 | N | Focal length for Band 2 (in mm) F12.7 |
| # 110 | 3138-3149 | N | Focal length for Band 3 (in mm) F12.7 |
| # 111 | 3150-3161 | N | Focal length for Band 4 (in mm) F12.7 |
| # 112 | 3162-3173 | N | Focal length for Band 5 (in mm) F12.7 |
| # 113 | 3174-3189 | N | BBR Coefficient for Band 2 for Scan F16.7(10 Vals) |
| # 114 | 3190-3333 | N | Repetition of field no 113 |
| # 115 | 3334-3349 | N | BBR Coefficient for Band 2 for Pixel F16.7(10 Vals) |
| # 116 | 3350-3493 | N | Repetition of field no 115 |
| # 117 | 3494-3509 | N | BBR Coefficient for Band 3 for Scan F16.7(10 Vals) |
| # 118 | 3510-3653 | N | Repetition of field no 117 |
| # 119 | 3654-3669 | N | BBR Coefficient for Band 3 for Pixel F16.7(10 Vals) |
| # 120 | 3670-3813 | N | Repetition of field no 119 |
| # 121 | 3814-3829 | N | BBR Coefficient for Band 4 for Scan F16.7(10 Vals) |
| # 122 | 3830-3973 | N | Repetition of field no 121 |
| # 123 | 3974-3989 | N | BBR Coefficient for Band 4 for Pixel F16.7(10 Vals) |
| # 124 | 3990-4133 | N | Repetition of field no 123 |
| # 125 | 4134-4149 | N | BBR Coefficient for Band 5 for Scan F16.7(10 Vals) |
| # 126 | 4150-4293 | N | Repetition of field no 125 |
| # 127 | 4294-4309 | N | BBR Coefficient for Band 5 for Pixel F16.7(10 Vals) |
| # 128 | 4310-4453 | N | Repetition of field no 127 |
| # 129 | 4454-4465 | N | MRC/PRC Angle for Roll/Pitch/Yaw F12.7(3 Vals) for AWiFS |
| # 130 | 4466-4489 | N | Repetition of field no 129 |
| # 131 | 4490-5304 |  | Spares |
| # 132 | 5305-6120 | A | For DPS Internal Use |

“nb” stands for no. of bands/CCD arrays.

+  Refer table 2.4.1.3 (Field No.10)

- Refer table 2.4.1.3 (Field No.10)

- # New Fields in Header Record of LGSOWG for IRS-P6

NOTE : Field 88b to88e will be repeated for maximum number of bands (for IRS-P6 it will be

TABLE 2.4.3.2

HEADER RECORD : DEFINITION/CONTENTS - (6120 Bytes)

( For IRS-1C/1D )

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("022 022 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Header Record sequence number -I4 |
| 5 | 17-20 | - | Blanks |
| 6 | 21-28 | N | Path Number (bbbbbPPP)-I8 |
| 7 | 29-36 | N | Row Number (bbbbbRRR)-I8 |
| 8 | 37-68 | A | Scene Identification-A32 + |
| 9 | 69-100 |  | Spares |
| 10 | 101-116 | N | Scene Centre Geographic location (lat) (Deg.) - F16.7 |
| 11 | 117-132 | N | Scene Centre Geographic location (long) (Deg.) F16.7 |
| 12 | 133-140 | N | Scene centre location within image (line no.) -I8 |
| 13 | 141-148 | N | Scene centre location within image (pixel no) - I8 |
| 14 | 149-164 | N | Left top corner geographic location of scene (lat) (Deg.) - F16.7 |
| 15 | 165-180 | N | Left top corner geographic location of scene (long) (Deg.) - F16.7 |
| 16 | 181-188 | N | Left Top corner location in scene (line no.) - I8 |
| 17 | 189-196 | N | Left top corner location in scene (pixel no.) - I8 |
| 18 | 197-212 | N | Right top corner geographic location (lat)-F16.7 |
| 19 | 213-228 | N | Right Top corner geographic location (long) - F16.7 |
| 20 | 229-236 | N | Right top corner location in scene (line no ) - I8 |
| 21 | 237-244 | N | Right top corner location in scene (pixel no)-I8 |
| 22 | 245-260 | N | Left bottom corner geographic location of scene (lat.)-F16.7 |
| 23 | 261-276 | N | Left bottom corner geographic location of scene (long)- F16.7 |
| 24 | 277-284 | N | left bottom corner location in scene (line no)-I8 |
| 25 | 285-292 | N | Left bottom corner location in scene (pixel no)-I8 |
| 26 | 293-308 | N | Right bottom corner geographic location of scene (lat)-F16.7 |
| 27 | 309-324 | N | Right bottom corner geographic location of scene (long)-F16.7 |
| 28 | 325-332 | N | Right Bottom corner location in scene (line no) -I8 |
| 29 | 333-340 | N | Right Bottom corner location in scene (pixel no) -I8 |
| 30 | 341-348 | N | Input nominal scene data (pixels)-I8 |
| 31 | 349-356 | N | Input nominal scene data (lines)-I8 |
| 32 | 357-364 | N | Input nominal pixel size at nadir - (meters) - F8.3 |
| 33 | 365-372 | N | Input nominal line spacing at nadir - (meters) - F8.3 |
| 34 | 373-388 | N | Input viewing angle (Deg.) - F16.7 |
| 35 | 389-396 | N | Input nominal pixels for SWIR band-I8 |
| 36 | 397-404 | N | Input nominal scans for SWIR band-I8 |
| 37 | 405-412 | N | Input nominal pixel size for SWIR band F8.3 |
| 38 | 413-420 | N | Input nominal line spacing for SWIRband I8 |
| 39 | 421-436 | N | Nominal orbit inclination (Deg.) - F16.7 |
| 40 | 437-452 | N | Nominal altitude (meters) - F16.7 |
| 41 | 453-468 | N | Longitude of ascending node, F16.7 |
| 41A | 469-470 | N | Endian Flag (0:for Big Endian, 1: Little Endian) |
| 41B | 471-472 | N | Shift percentage( 0 -99) I2, for shift along track products, I2 |
| 41C | 473-474 | N | Quadrant Number (Valid for Quadrant products only), I2 |
| 41D | 475-501 | - | Spares |
| 42 | 502-517 | N | Satellite heading angle (Deg.) - F16.7 |
| 43 | 518-525 | N | Orbit Number, I8 |
| 44 | 526-541 | N | Instantaneous Cross track FOV in radians -F16.7 |
| 45 | 542-573 | - | Spares |
| 46 | 574-589 | N | Sun angle (Azimuth) (Deg.) – F16.7 |
| 47 | 590-605 | N | Sun angle (elevation) (Deg.) F16.7 |
| 48 | 606-621 | N | Predicated scene center latitude (deg.) F16.7 |
| 49 | 622-637 | N | Predicated scene centre longitude (deg.) F16.7 |
| 50 | 638-653 | N | Observed scene center latitude (deg.) F16.7 |
| 51 | 654-669 | N | Observed scene center longitude (deg.) F16.7 |
| 52 | 670-797 | - | Spares |
| IMAGING PARAMETERS |
| 53 | 798-829 | A | Input scene start time (HH:MM:SS: mmm) |
| 54 | 830-845 | A | Mission identification-A16 |
| 55 | 846-877 | A | Sensor identification – A32 |
| 56 | 878-893 | A | Spectral mode – A16 |
| 57 | 894-913 |  | Spares |
| 58 | 914-929 | N | Day number within cycle-I16 |
| 59 | 930-937 | N | Payload tilt step number - I8 |
| 60 | 938-945 | N | Payload tilt per step in (Deg) - F8.3 |
| 61 | 946-961 | N | LISS-3 scene centre lat. corresponding to PAN - F 16.7 |
| 62 | 962-977 | N | LISS-3 scene centre long. corresponding to PAN - F 16.7 |
| 63 | 978-985 | N | LISS-3 Path no. Corresponding to PAN- I8 |
| 64 | 986-993 | N | LISS-3 Row no. Corresponding to PAN- I8 |
| 65 | 994-1009 | N | Integration Time for SWIR band - F 16.7 |
| 66 | 1010-1025 | N | Integration Time (in milli sec) - F 16.7 |
| 67 | 1026-1088 |  | Spares |
| 68 | 1089-1104 | N | On board gain number "nb" I4 |
| 69 | 1105-1112 |  | Spares |
| 70 | 1113-1120 | N | Number of spectral bands-I8 |
| 71 | 1121-1152 | N | Lower and upper limit of wavelength range in nanometers range in nanometers 2"nb" F4.2 where nb = no. of bands in the sensor. |
| 72 | 1153-1216 | N | CCD temp for all the CCD arrays present in sensor "nb" F8.4 (in degree Celsius) |
| 73 | 1217-1280 | - | Minimum (LMIN) & Maximum (LMAX) radiance for number of bands present in the product 2"nb" F8.5 (mw/sq. cm / str / micromet) |
| Conversion formula for Digital Count to radiance is as follows. Lrad = (DN/MaxGray)*(Lmax - Lmin) + Lmin. Lrad : Radiance for a given DN value. DN : Digital Count MaxGray : IRS-1C/1D : 63 for PAN & 127 for WiFS & LISS-3 for Raw Products only. 255 for Corrected products. Lmin/Lmax: Minimum/Maximum radiance value for a given band. |
| IMAGE DATA PARAMETERS |
| 74 | 1281-1296 | N | Number of image pixels per line-I16 |
| 75 | 1297-1312 | N | Number of image data lines-I16 |
| 76 | 1313-1320 | N | Processed pixel spacing F8.3 |
| 77 | 1321-1328 | N | Processed line spacing F8.3 |
| 78 | 1329-1344 | A | Interleaving indicator-A16 |
| 79 | 1345-1360 | N | Spectral bands indicator - 4I4 |
| 80 | 1361-1368 | N | Processed pixel spacing for SWIR band F8.3 |
| 81 | 1369-1376 | N | Processed line spacing for SWIR band-F8.3 |
| 82 | 1377-1392 | N | Number of Image pixels per line for SWIR band - I16 |
| 83 | 1393-1409 | N | Number of Image data line for SWIRband - I16 |
| 84 | 1409-1440 |  | Spares |
| 85 | 1441-1456 | A | Preprocessing level identification-A16 LEVEL-0 : for RAW Products LEVEL-1 : for RAD Products (Radiometric Correction only) LEVEL-2 : for Radiometric Correction + Systematic Geometric Correction LEVEL-3 : Precision Corrected |
| 86 | 1457-1464 | A | Radiometric calibration designator-A8 DONE : for Radiometrically corrected products NOT DONE : for RAW products. |
| 87 | 1465-1472 | A | Resampling designator -I8 |
| 88 | 1473-1632 | - | Spares |
| 89 | 1633-1648 | N | Number of lines losses "nb"I4 |
| 90 | 1649-1664 | N | Number of dead detectors "nb"I4 |
| 91 | 1665-1669 | A | Multi Scene/Sensor flag (TRUE or FALSE) - A5 |
| 92 | 1670-1675 | N | No. of Mosaicked or merged scenes I6 |
| 93 | 1676-1707 | A | Second scene identification A32 |
| 94 | 1708-1713 | A | Second scene satellite identification A6 |
| 95 | 1714-1721 | N | Second scene input nominal resolution (meters) F8.3 |
| 96 | 1722-1737 | N | Second scene sun elevation angle (deg.) - F16.7 |
| 97 | 1738-1753 | N | Second scene sun azimuth angle (deg.) - F16.7 |
| 98 | 1754-1769 | N | Observed scene centre latitude (deg.) - F16.7 |
| 99 | 1770-1785 | N | Observed scene centre longitude (deg.) - F16.7 |
| 100 | 1786-1801 | N | Second scene heading angle (deg.) - F16.7 |
| 101 | 1802-1817 | N | Predicted second scene centre latitude (deg.) - F16.7 |
| 102 | 1818-1833 | N | Predicted Second Scene Centre Longitude (deg.) - F16.7 |
| 103 | 1802-3046 |  | Repetition of field no. 93,94,95,96,97,98,99,100,101,102 for remaining number of scenes. |
| 104 | 3047-6120 | - | Spares |

"nb" stands for no. of bands/CCD arrays.

+  Refer table 2.4.1.3 (Field No.10)

- Refer table 2.4.1.3 (Field No.10)

TABLE 2.4.3.3

EPHEMERIES/ATTITUDE RECORDS

(DEFINITION/CONTENTS) (6120 Bytes)

(For IRS-P6)

| FIELD NO | BYTE NUMBER | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes (“366 044 022 022”) |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in Ephemeries and attitude records – I4 |
| 5 | 17-20 | N | Number of Ephemeris/Attitude/Q’s values in this record – I4 (Maximum 20 values will be present) |
| 6 | 21-32 | N | Satellite position_X- F12.4 ( kms) |
| # 7a. | 33-260 | N | Repetition of field no 6 for more positions |
| # 7b | 261-500 | - | Spares |
| 8. | 501-512 | N | Satellite position_Y- F12.4 ( kms) |
| # 9a | 513-740 | N | Repetition of field no 8 for more positions |
| # 9b | 741-980 | - | Spares |
| 10 | 981-992 | N | Satellite position_Z- F12.4 ( kms) |
| # 11a | 993-1220 | N | Repetition of field no 10 for more positions |
| # 11b | 1221-1460 | - | Spares |
| 12 | 1461-1472 | N | Velocity vector_X- F12.7 ( km/sec) |
| # 13a | 1473-1700 | N | Repetition of field no – 12 |
| # 13b | 1701-1940 | - | Spares |
| 14 | 1941-1952 | N | Velocity vector_Y – F12.7 ( km/sec) |
| # 15a | 1953-2180 | N | Repetition of field no 14 |
| # 15b | 2181-2420 | - | Spares |
| 16 | 2421-2432 | N | Velocity vector_Z – F12.7 ( km/sec) |
| # 17a | 2433-2660 | N | Repetition of field no 16 |
| # 17b | 2661-2900 | - | Spares |
| # 18a | 2901-2912 | N | Q1 – F12.7 Q=Quaternion |
| # 18b | 2913-3140 | N | Repetition of Q1 |
| # 18c | 3141-3152 | N | Q2 – F12.7 |
| # 18d | 3153-3380 | N | Repetition of Q2 |
| # 18e | 3381-3392 | N | Q3 – F12.7 |
| # 18f | 3393-3620 | N | Repetition of Q3 |
| # 18g | 3621-3632 | N | Q4 – F12.7 |
| # 18h | 3633-3860 | N | Repetition of Q4 |
| # 18i | 3861-4012 | - | Spares |
| 19 | 4013-4028 | N | Satellite Altitude (meters) – F16.7 |
| 20 | 4029-4054 | A | Scene centre time – A 26 (HH:MM:SS:sss) |
| 21 | 4055-4066 | A | Ephemeries/Attitude start time A12 (HH:MM:SS:SSS) |
| 22 | 4067-4072 | N | Time interval for Ephemeries/Attitude values F6.3 in seconds for 1C/1D, in milli seconds for P6 |
| 23 | 4073-4100 |  | Spares |
| 24 | 4101-4110 | N | Yaw (deg.) – F10.5 |
| # 25 | 4111-4300 | - | Repetition of field no 24 |
| # 25a | 4301-4500 |  | Spares_Yaw |
| 26 | 4501-4510 | N | Roll (deg.) – F10.5 |
| # 27 | 4511-4700 | - | Repetition of field no 26 |
| # 27a | 4701-4900 |  | Spares_Roll |
| 28 | 4901-4910 | N | Pitch (deg.) – F10.5 |
| # 29 | 4911-5100 | - | Repetition of field no 28 |
| # 29a | 5101-5300 |  | Spares_Pitch |
| 30 | 5301-5310 | N | Scene centre Yaw (deg.) F10.5 |
| 31 | 5311-5320 | N | Scene centre Roll (deg.) F10.5 |
| 32 | 5321-5330 | N | Scene centre Pitch (deg.) F10.5 |
| # 33a | 5331-5342 | N | Sidereal angle in degrees F12.7 |
| # 33b | 5343-5570 | - | Repetition of field no 33a |
| # 33c | 5571-6115 |  | Spares |
| # 33d | 6116-6118 | N | Star/Earth Sensor RPY Flag 0=Ground Attitude Determination not possible 1=ADAGE determined Q’s(ES+GYRO) 2=ADJUST determined Q’s(defau)(STAR SEN) 3=AOCE determined Q’s |
| 34 | 6119-6120 | A | Swath Flag (00/01) 01 : Swath Model Done 00 : Swath Model Not Done |

Note :    Number of Ephemeries/Attitudes values in each record will be as per the field no.5

TABLE 2.4.3.3

EPHEMERIES/ATTITUDE RECORDS

(DEFINITION/CONTENTS) (6120 Bytes)

( For IRS-1C/1D )

| FIELD NO | BYTE NUMBER | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("366 044 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in Ephemeries and attitude records - I4 |
| 5 | 17-20 | N | Number of Ephemeries/Attitude values in this record - I4 |
| 6 | 21-32 | N | Satellite position_X- F12.4 ( kms) |
| 7. | 33-500 | - | Repetition of field no 6 for more positions |
| 8. | 501-512 | N | Satellite position_Y- F12.4 ( kms) |
| 9 | 513-980 | - | Repetition of field no 8 for more positions |
| 10 | 981-992 | N | Satellite position_Z- F12.4 ( kms) |
| 11 | 993-1460 |  | Repetition of field no 10 for more positions |
| 12 | 1461-1472 | N | Velocity vector_X- F12.7 ( km/sec) |
| 13 | 1473-1940 | - | Repetition of field no – 12 |
| 14 | 1941-1952 | N | Velocity vector_Y - F12.7 ( km/sec) |
| 15 | 1953-2420 |  | Repetition of field no 14 |
| 16 | 2421-2432 | N | Velocity vector_Z - F12.7 ( km/sec) |
| 17 | 2433-2900 | - | Repetition of field no 16 |
| 18 | 2901-4012 |  | Spares |
| 19 | 4013-4028 | N | Satellite Altitude ( meters) - F16.7 |
| 20 | 4029-4054 | A | Scene centre time - A 26 (HH:MM:SS:sss) |
| 21 | 4055-4066 | A | Ephemeries/Attitude start time A12 (HH:MM:SS:SSS) |
| 22 | 4067-4072 | N | Time interval for Ephemeries/Attitude values F6.3 in seconds for 1C/1D, in milli seconds for P6 |
| 23 | 4073-4100 |  | Spares |
| 24 | 4101-4110 | N | Yaw (deg.) - F10.5 |
| 25 | 4111-4500 | - | Repetition of field no 24 |
| 26 | 4501-4510 | N | Roll (deg.) - F10.5 |
| 27 | 4511-4900 | - | Repetition of field no 26 |
| 28 | 4901-4910 | N | Pitch (deg.) - F10.5 |
| 29 | 4911-5300 | - | Repetition of field no 28 |
| 30 | 5301-5310 | N | Scene centre Yaw (deg.) F10.5 |
| 31 | 5311-5320 | N | Scene centre Roll (deg.) F10.5 |
| 32 | 5321-5330 | N | Scene centre Pitch (deg.) F10.5 |
| 33 | 5331-6118 | - | Spares |
| 34 | 6119-6120 | A | Swath Flag (00/01) 01 : Swath Model Done 00 : Swath Model Not Done |

Note :    Number of Ephemeries/Attitudes values in each record will be as per the field no.5

TABLE  2.4.3.4

(*) CALIBRATION RECORDS : DEFINITIONS/CONTENTS (6120 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("077 044 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record Sequence number in calibration record-I4 |
| 5 | 17-20 | - | Spares |
| 6 | 21-24 | N | Spectral band number - I4 |
| 7 | 25-28 | N | Gain or Dark current/bias flag (bbb1 or bbb2) - I4 |
| 8 | 29-33 | N | Number of the detector corresponding to the 1st value in this record – I5 |
| 9 | 34-36 |  | Spares |
| 10 | 37-41 | N | Number of the detector corresponding to the last value in this record – I5 |
| 11 | 42-44 | - | Spares |
| 12 | 45-48 | N | Number of the dead detectors within the 6000 or 4096 or 2100 detectors - I4 |
| 13 | 49-60 | - | Spares |
| 14 | 61-6060 | B | Value given is multiplied by 100 (for IRS-P6 otherwise multiplied by 1000 for IRS-1C/1D) 3000 values for gain & bias. (16 bit binary No.is used for gain or bias coded in Integer * 2) |
| 15 | 6061-6120 | - | Spares |

(*) Contents applicable for RAW and Radiometrically corrected products.

Gain or bias value (999) will represent the dead detector in the array.

TABLE 2.4.3.5

MAP PROJECTION RECORD - DEFINITION/CONTENTS (6120 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type & subtype octal codes ("044 044 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in map projection record I4 |
| 5 | 17-20 | - | Spares |
| 6 | 21-26 | A | Map projection identifier - A6 |
| 7 | 27-42 | A | Name of reference ellipsoid-A16 |
| 8 | 43-58 | N | Semi major axis of geoid (km) - F16.7 |
| 9 | 59-74 | N | Eccentricity of the geoid - F16.7 |
| 10 | 75-314 | N | Map Projection parameters - 15 F16.7 Ref. APPENDIX-IB |
| #11 | 315-320 | I6 | Total grid points |
| #12 | 321-326 | I6 | Total Grid points in this record |
| #13 | 327-332 | I6 | Scan Line |
| #14 | 333-338 | I6 | Pixel Number |
| #15 | 339-354 | F16.5 | Latitude in degree/ Northing in meter(for UTM) |
| #16 | 355-370 | F16.5 | Longitude in degree/ Easting in meter(for UTM) |
| #17 | 371-386 | F16.7 | Sun Elevation in degree |
| #18 | 387-402 | F16.7 | Sun Azimuth in degrees |
| #19 | 403-418 | F16.7 | Satellite Elevation angle in degree |
| #20 | 419-434 | F16.7 | Satellite Azimuth angle in degree |
| #21 | 435-6050 | - | Repetition of field no. 13 to 20 for maximum 53 values. |
| #22 | 6051-6100 | A | Name of reference Datum-A50 (Ref. APPENDIX-1D) |
| #23 | 6101-6120 |  | Spares |

#   New Fields in Map Projection Record of LGSOWG for P6

NOTE : Field no. 13 to 20 will be repeated for total grid points in this record (field no. 12 Maxium 53 such values will be accommodated in a single map projection record of 6120 bytes. In case the total grid points(field no 11) exceeds 53. more map projection records will be present

TABLE 2.4.3.6

HISTOGRAM RECORDS DEFINITION/CONTENTS (6120 Bytes)

| FIELD NO | BYTE NO | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("300 044 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in Histogram - I4 |
| 5 | 17-20 | N | Number of Histogram samples in this Record |
| 6 | 21-24 | N | Spectral Band number - I4 |
| 7 | 25-26 | N | Sampling rates along pixels - I2 |
| 8 | 27-28 | - | Spares |
| 9 | 29-30 | N | Sampling rates along scan lines - I2 |
| 10 | 31-32 | - | Spares |
| 11 | 33-5152 | N | Histogram values - I10 For Raw (0-63 1C/1D PAN 0-127 1C/1D/P6 L3 0-127 1C/1D/P6 L4 0-1023 P6 AWiFs ) For GEO(0-255 L3,L4,PAN 0-1023 AWiFs) |
| 12 | 5153-6120 | - | Spares |

TABLE 2.4.3.7

GCP RECORDS : DEFINITION/CONTENTS (6120 Bytes)

| FIELD NO | BYTE NO | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within the file |
| 2 | 5-8 | B | Record type and subtype octal codes ("011 044 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in GCP records (bbb1) - I4 |
| 5 | 17-20 | N | Number of GCPs - I4 |
| 6 | 21-6120 | - | Spares |

TABLE  2.4.3.8

ANNOTATIONS RECORD : DEFINITIONS/CONTENTS (6120 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within file |
| 2 | 5-8 | B | Record type and subtype octal codes ("022 333 022 022") |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Record sequence number in annotation record - I4 |
| 5 | 17-20 | N | Number of annotation segments in this record (bbb4) - I4 |
| 6 | 21-52 |  | Spares |
|  |  |  | (Segment 1) |
| 7 | 53-56 | N | Segment length - I4 |
| 8 | 57-60 | N | Length of the character string - I4 |
| 9 | 61-64 | A | Identifier - A4 |
| 10 | 65-100 | - | Spares |
| 11 | 101-180 | A | Title for top annotation line 1 - A80 |
| 12 | 181-232 | - | Spares |
|  |  |  | (Segment 2) |
| 13 | 233-236 | N | Segment length - I4 |
| 14 | 237-240 | N | Length of this character string - I4 |
| 15 | 241-244 | A | Identifier - A4 |
| 16 | 245-300 | - | Spares |
| 17 | 301-380 | A | Title for top annotation line 2- A80 |
| 18 | 381-412 | - | Spares |
|  |  |  | (Segment 3) |
| 19 | 413-416 | N | Segment length - I4 |
| 20 | 417-420 | N | Length of this character string - I4 |
| 21 | 421-424 | A | Identifier - A4 |
| 22 | 425-500 |  | Spares |
| 23 | 501-580 | A | Title for top annotation line -3 - A80 |
| 24 | 581-612 | - | Spares |
|  |  |  | (Segment 4) |
| 25 | 613-616 | N | Segment Length -I4 |
| 26 | 617-620 | N | Length of the character string -I4 |
| 27 | 621-624 | A | Identifier - A4 |
| 28 | 625-700 | - | Spares |
| 29 | 701-780 | A | Title for bottom annotation line -A80 |
| 30 | 781-1700 | - | Spares |
| 31 | 1701-1716 | N | Tick mark interval (degree) - F16.7 |
|  |  |  | Geographic reference marks |
| 32 | 1717-1720 | N | Number of segment "Geographic reference marks" - I4 |
| 33 | 1721-1722 | N | Length of geographic character annotation string - I2 |
| 34 | 1723-1724 | - | Spares |
|  |  |  | Top Geographic reference mark |
| 35 | 1725-1728 | A | Nature of mark - A4 (TOP/BOT/LEFT/RIGH) |
| 36 | 1729-1730 | N | Number of top marks - I2 |
| 37 | 1731-1736 | N | Line Number - I6 |
| 38 | 1737-1742 | N | Pixel Number - I6 |
| 39 | 1743-1750 | A | Geographic annotation - A8 (e.g. E100: 30) |
| 40 | 1751-2730 | - | Repetition of field No.37, 38 and 39 for no. of top marks |
| 41 | 2731-2764 | - | Spares |
|  |  |  | Left Geographic reference mark |
| 42 | 2765-2768 | A | Nature of mark - A4 |
| 43 | 2769-2770 | N | Number of left marks - I2 |
| 44 | 2771-3770 | - | Repetition of field No. 37,38 and 39 for No. of left marks |
| 45 | 3771-3783 |  | Spares |
|  |  |  | Right Geographic reference mark |
| 46 | 3784-3787 | A | Nature of mark - A4 |
| 47 | 3788-3789 | N | Number of right marks - I2 |
| 48 | 3790-4789 |  | Repetition of field No. 37,38 and 39 for No.of Right marks. |
| 49 | 4790-4800 | - | Spares |
|  |  |  | Bottom Geographic reference mark |
| 50 | 4801-4804 | A | Nature of mark - A4 |
| 51 | 4805-4806 | N | Number of bottom marks - I2 |
| 52 | 4807-5806 |  | Repetition of field No. 37,38 and 39 for No. of Bottom marks |
| 53 | 5807-6120 | - | Spares |

TABLE 2.4.3.9

(+) PIXEL & LINE LOOKUP TABLE : DEFINITION/CONTENTS(6120 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1. | 1-4 | B | The record number of this record within the file |
| 2. | 5-8 | B | Record type and subtype octal codes ("025 333 022 022") |
| 3. | 9-12 | B | Length of this record (6120) |
| 4. | 13-16 | N | Record sequence no in line lookup table record I4 |
| 5. | 17-20 |  | Spares |
| 6. | 21-28 | N | Tilt angle (deg.) F8.5 |
| 7. | 29-32 | N | No of pixel increment due to panoramic distortion - I4 |
| 8. | 33-40 |  | Spares |
| 9. | 41-46 | N | Total scan line increment pointer - I6 |
| 10. | 47-99 | - | Spares |
| 11. | 100-101 | B | Line lookup table values |
| 12. | 102-1099 | B | For remaining no of line increment points |
| 13. | 1100-1599 | - | Spares |
| 14. | 1600-1605 | N | Total pixel increment pointer – I6 |
| 15. | 1606-1653 | - | Spares |
| 16. | 1654-1655 | B | Pixel Lookup table values |
| 17. | 1656-5653 | B | Repetition of field no 16 for remaining no.of pixel increment pointer |
| 18. | 5654-6120 | - | Spares |

(+)  Content is applicable for basic stereo product.

Field no 7 to 18 are not valid for IRS-P6.

TABLE 2.4.3.10

ATTITUDE RATE RECORD : DEFINITION/CONTENTS (6120 bytes)

| Field No. | Byte No | Type | Definition |
| --- | --- | --- | --- |
| 1. | 1-4 | B | Record no of this record in this file |
| 2. | 5-8 | B | Record Type and sub-type octal codes (“026 044 022 022”) |
| 3. | 9-12 | B | Length of this record |
| 4. | 13-16 | N | Record sequence no in this record –I4 |
| 5. | 17-20 | N | Total no of Attitude Rate values in this record. |
| 6. | 21-32 | A | Attitude rate start time (HH:MM:SS:sss) A12` |
| 7. | 33-38 | - | Spares |
| 8. | 39-44 | N | Rate interval (in milliseconds)F6.3 |
| 9. | 45-54 | N | Roll Rate (degree/second)- F10.7 |
| 10. | 55-64 | N | Pitch Rate (degree/second) – F10.7 |
| 11. | 65-74 | N | Yaw Rate (degree/second)- F10.7 |
| 12. | 75-6044 | - | Repetition of field 9, 10, & 11 for more rate values. |
| 13. | 6045-6120 | - | Spares |

Note:  Number of Attitude Rate values in each record will be as per the field no.5.

TABLE 2.4.3.11

(*) BOUNDARY RECORD : DEFINITION/CONTENT (6120 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Number of this record in this file |
| 2 | 5-8 | B | Record type and subtype octal codes (“023 333 022 022”) |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Boundary record sequence number – I 4 |
| 5 | 17-20 | - | Spares |
| 6 | 21-24 | B | Total no of boundary points |
| 7 | 25-30 | A | Start scan line no. - I6 |
| 8 | 31-n*x2+30 | B | Pixel number |
| 9 | n*x 2 + 31- n x 2 +32 | B | Increment flag for the next scan line (-1) |
| 10 | n*x 2 + 33 – 6120 | B | Repetition of field no 8 & 9, for more no of boundary points |

(*) n represents the no of pixels on the scan line.

Note: -99 will mark the end of this record.

TABLE 2.4.3.12

BOUNDARY ANNOTATION RECORD : DEFINITION/CONTENTS (6120 bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record Number of this record in this file |
| 2 | 5-8 | B | Record type & subtype octal codes (“024 333 022 022”) |
| 3 | 9-12 | B | Length of this record (6120) |
| 4 | 13-16 | N | Boundary annotations record sequence no. (bbb1) – I4 |
| 5 | 17-20 | - | Spares |
| 6 | 21-24 | N | No. of annotations – I4 |
| 7 | 25-32 | N | Scan Line no. – I8 |
| 8 | 33-40 | N | Pixel no. – I8 |
| 9 | 41-72 | A | Character string – A 32 |
| 10 | 73-6120 | - | Repetition of field no. 7,8 & 9 for other annotations. |

### 2.4.4 IMAGE DATA FILE

1.File descriptor Record

2. Image data Records

TABLE 2.4.4.1

FILE DESCRIPTOR RECORD : DEFINITIONS/CONTENTS (540 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-180 |  | Refer Table No.2.4.2.1. (Fixed part of the file descriptor record) |
|  |  |  | VARIABLE SEGMENT |
| 2 | 181-186 | N | Number of image records – I6 |
| 3 | 187-192 | N | Image record length – I6 |
| 4 | 193-216 | - | Spares |
|  |  |  | PIXEL GROUP DATA |
| 5 | 217-220 | N | Number of bits per pixel (e.g. bbb7) – I4 |
| 6 | 221-224 | N | Number of pixels per data group – I4 |
| 7 | 225-228 | N | Number of byte per data group (bbb1) – I4 |
| 8 | 229-232 | A | Justification and order of pixels within data group (RJLR) –A4 |
|  |  |  | IMAGE DATA |
| 9 | 233-236 | N | Number of image (Bands) – I4 |
| 10 | 237-244 | N | Number of lines per image (Excluding top and bottom border lines) – I8 |
| 11 | 245-248 | N | Number of left border pixels per line – I4 |
| 12 | 249-256 | N | Number of image pixels per line – I8 |
| 13 | 257-260 | N | Number of right border pixels per line – I4 |
| 14 | 261-264 | N | Number of top border lines – I4 |
| 15 | 265-268 | N | Number of bottom border lines – I4 |
| 16 | 269-272 | A | Interleaving indicator – A4 |
|  |  |  | RECORD DATA IN THIS FILE |
| 17 | 273-274 | N | Number of physical records per line – I2 |
| 18 | 275-276 | N | Number of physical records per multi-spectral line –I2 |
| 19 | 277-280 | N | Number of bytes of prefix data per record – I4 |
| 20 | 281-288 | N | Number of bytes of image data per record – I8 |
| 21 | 289-292 | N | Number of bytes of suffix data per record – I4 |
| 22 | 293-296 | A | Prefix suffix repeat flag – A4 |
|  | PREFIX/SUFFIX DATA LOCATORS |
|  | The following fields are prefix/suffix data locaters. The location is given in 8 bytes as follows: 4 bytes – giving the byte number within the prefix or suffix which begins the field to be located 2 bytes – giving the length in bytes of the field to be located 1 byte - the letter P or S coded in this byte indicates that the information is in the scan line prefix or suffix, respectively 1 byte - a code indicating the type of data in the field coded are (A = Alphanumeric,B = Binary, N = Numeric) |
| 23 | 297-304 | A | Scan line number locator – A8 |
| 24 | 305-312 | A | Image (Band) number locator – A8 |
| 25 | 313-320 | A | Time of scan line locator – A8 |
| 26 | 321-328 | A | Left-fill count locator – A8 |
| 27 | 329-336 | A | Right-fill count locator – A8 |
| 28 | 337-440 | - | Spares |
| 29 | 441-448 | N | Maximum data range of pixels (starting from `0’ to 255/127/63) – I8 |
| 30 | 449-540 | - | Spares |

TABLE 2.4.4.2

IMAGE DATA RECORDS : DEFINITION/CONTENTS

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record sequence number of this record within the file |
| 2 | 5-8 | B | Record type and subtype octal codes (“355 355 022 022”) |
| 3 | 9-12 | B | Length of this record |
| 4 | 13-16 | B | Scanline Number |
| 5 | 17-18 |  | Spares |
| 6 | 19-20 | B | Band number |
| 7 | 21-32 | - | Spares |
| 8 | 33-(32+np)=X | B | Image data |
| 9 | (X+1) - (X+18) | - | Spares |
| 10 | (X+19) to totB | - | Spares |

Note :

np   => Field no. 12 variable segment of file descriptor  record.

TotB => Field no. 3 of variable segment of file descriptor record.

### 2.4.5 TRAILER FILE

- Trailer file descriptor Record

2. Trailer Records

TABLE 2.4.5.1

TRAILER FILE DESCRIPTOR : DEFINITION/CONTENTS (360 bytes)

| FIELD NO | BYTE NO | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-180 | - | see table no 2.4.2.1 (fixed part of the file descriptor record) |
| 2 | 181-184 | N | Number of trailer records in the file – (I4) |
| 3 | 185-188 | N | Length in bytes of the trailer records (b 360) – I4 |
| 4 | 189-360 | - | Spares |

TABLE  2.4.5.2

TRAILER RECORD : DEFINITION/CONTENTS (360 Bytes)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record number of this record within the file |
| 2 | 5-8 | B | Record type and subtype octal codes (“022 366 022 022”) |
| 3 | 9-12 | B | Length of this record (360 Bytes) |
| 4 | 13-16 | N | Record sequence number in trailer records (bbbN) – I4 |
| 5 | 17-20 | - | Spares |
| 6 | 21-35 | N | Cloud cover values giving percent cloud cover in different parts of the picture 3 bytes/value) – 5I3 |
| 7 | 36-95 |  | Spares |
| 8 | 96-99 | N | No. of parity errors for corresponding band no. – I4 |
| 9 | 100-103 | N | No. of remaining lines loses in the scene for corresponding band no. – I4 |
| 10 | 104-107 | N | Line losses mir |
| 11 | 108-360 | - | Spares |

### 2.4.6  NULL FILE

1.  Null volume descriptor record.

TABLE 2.4.6.1

NULL VOLUME DESCRIPTOR RECORD : DEFINITIONS/CONTENTS (360 BYTES)

| FIELD NO. | BYTE NO. | TYPE | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | 1-4 | B | Record sequence number in this file (1) |
| 2 | 5-8 | B | Record type and subtype octal codes ("022 300 077 022") |
| 3 | 9-12 | B | Length of this record (360 bytes) |
| 4 | 13-14 | A | ASCII/EBCDIC flag - (Ab) |
| 5 | 15-16 | - | Spares |
| 6 | 17-28 | A | Super structure control document number-A12 |
| 7 | 29-30 | N | Control document revision number - I2 |
| 8 | 31-32 | A | Control document revision letter - A2 |
| 9 | 33-44 | A | Software release number -, A12 |
| 10 | 45-60 | A | Physical tape ID - A16 |
| 11 | 61-76 | A | Logical volume ID - A16 |
| 12 | 77-92 | A | Logical volume set ID - A16 |
| 13 | 93-94 | N | Number of physical volume in the set - I2 |
| 14 | 95-96 | N | Physical volume number : Start of logical volume - I2 |
| 15 | 97-98 | N | Physical volume number : End of logical volume - I2 |
| 16 | 99-100 | N | Physical volume no. containing this descriptor - I2 |
| 17 | 101-104 | N | First file no. referenced in this physical volume - I4 |
| 18 | 105-108 | N | Logical volume No. within volume set - I4 |
| 19 | 109-112 | N | Logical volume No. within physical Volume - I4 |
| 20 | 113-360 | - | Spares |

RECORD TYPE AND SUBTYPE CODES FOR LGSOWG

IRS DATA PRODUCTS

| RECORDS | BYTE 5 (Octal) | BYTE 6 (Octal) | BYTE 7 (Octal) | BYTE 8 (Octal) |
| --- | --- | --- | --- | --- |
| Volume Descriptor | 300 | 300 | 022 | 022 |
| File Pointer | 333 | 300 | 022 | 022 |
| Text | 022 | 077 | 022 | 022 |
| File Descriptor | 077 | 300 | 022 | 022 |
| Header | 022 | 022 | 022 | 022 |
| Ephemeris/Attitude | 366 | 044 | 022 | 022 |
| Calibration | 077 | 044 | 022 | 022 |
| Histogram | 300 | 044 | 022 | 022 |
| Map projection | 044 | 044 | 022 | 022 |
| GCPs | 011 | 044 | 022 | 022 |
| Annotation | 022 | 333 | 022 | 022 |
| Boundary | 023 | 333 | 022 | 022 |
| Boundary Annotation | 024 | 333 | 022 | 022 |
| Lookup table | 025 | 333 | 022 | 022 |
| Attitude Rate | 026 | 044 | 022 | 022 |
| Image Data | 355 | 355 | 022 | 022 |
| Trailer | 022 | 366 | 022 | 022 |
| Null Volume Descriptor | 022 | 300 | 077 | 022 |

FIGURE – 1: LAYOUT OF SUPER STRUCTURE FORMAT IN DAT

FILE NUMBER        CONTENTS                	FILE NAME

File 0        	: Volume Descriptor

: File Pointer (1)        		Volume Directory

: File Pointer (2)

: File Pointer (3)

: Text

EOF (x)

File 1         	: Leader file Descriptor

: Header Record           	Leader file

: Ancillary Record

: Annotation Record

: Boundary Record

EOF (x)

File 2          	: Imagery file descriptor

: Image data records      	Imagery file

EOF (x)

File 3          	: Trailer file Descriptor

: Trailer records         		Trailer file

EOF (x)

File NULL       	: NULL Volume Descriptor  	Null Volume

Directory file

EOF

EOF

EOF

(x) EOF = End of file tape mark

LIST OF ACRONYMS TO BE USED

SATELLITE                    SENSOR

1C   IRS-1C                        	3    LISS-III

A    PAN-A

B    PAN-B

C    PAN-C

D    PAN-D

M    MIR

W    WIFS

1D   IRS-1D                            LISS-IV

P6  IRS-P6                              3	LISS-III

M	LISS-IV (MONO)

MX	LISS-IV (MX)

W	AWiFS

SUBSCENES

PAN-A     	|

|

PAN-B     	|

IRS-1C/1D/P6     ------>            			|------>1, 2, 3, 4, 5,

PAN-C     	|        	6, 7, 8, 9

|

PAN-D     	|

IRS-P6      ------->           L4M	- A,B,C,D

L4X

PROJECTION

O    NO PROJECTION

P    POLYCONIC

S    SOM

U    UTM (Ref. ellip-Int)

V    UTM (Ref. ellip-Clarke)

R    STEREOSCOPIC

L    LAMBERTS' conformal

conical proj

RESAMPLING                  	ENHANCEMENTS

O    NO SAMPLING                   	00   NO ENHANCEMENTS

B    BILINEAR                      		01   CORRECTED

C    CC                            		02   HIST EQ

D    DS 16

N    NN

K	   KAISER

PROC LEVEL               		DATA FORMAT

3    PRECISION

2    BULK                          		6    BIL

1    RAD                            		7    BSQ

0    RAW         				B    Fast Format Rev. C

T    GeoTIFF (Grey Scale)

R    GeoTIFF (RGB)

H    HDF

# APPENDIX – 1A: CLARIFICATION OF EXISTING FORMAT

Volume Directory File

- Volume Descriptor Record:

In Field No 10 the Symbol U = C/T/D represents

C : For Compact Disk (CD).

D : For DATs (both 4mm & 8mm) of different Capacity.

U : For Other Output Media.

Z:  DISK

Leader File

- Calibration Record:

This record is valid only for RAW products only.

- GCP Record:

This record is not valid for geometrically uncorrected (RAW & RAD) products.This is a dummy record.

- Annotations Record:

Annotation titles from field no 5 to field no. 30 are relevant for photo products only.

- Boundary Annotation Record:

This record is currently not applicable for IRS   products. So now dummy record has been put.

- Pixel & Line Lookup table Record:

Valid for Basic stereo products, for other products one dummy record will be there.

- Attitude Rate Record:

It is relevant for geometrically uncorrected (RAW & RAD) products. (for IRS-1C/1D only). For IRS-P6 this is a dummy record.

  - Field No. 6 Byte No 21-32 Attitude rate start time is in HH:MM:SS: mmm, A12 format.

- Boundary Record:

This record is currently not applicable for IRS products. So now dummy record has been put.

NOTE:

1. All time information except product creation time is given in UT. Scene covered by Indian region will have IST for scene at field no.20 of Ephemeris/attitude record of Leader file.

2. Conversion formula for Digital Count to radiance is as follows.

Lrad = (DN/MaxGray)*(Lmax-Lmin) + Lmin

Where

Lrad :Radiance for a given DN value.

DN   :Digital Count

MaxGray:IRS-1C/1D : 63 for PAN & 127 for WiFS & LISS-3 for Raw Products only.

255 for Corrected products.

IRS-P6 : 127 for LISS-4 and LISS-3 and 1023 for AWiFS.

Lmin/Lmax :minimum/Maximum radiance value for a given bias.

# APPENDIX – 1B: USGS Projection Parameters

Fast Format Revision C Supports 17 USGS projections. For all projections except State Plane, USGS parameters 1 and 2 are semi major and minor axes of the requested earth ellipsoid. This has been adapted for Super Structure (LGSOWG) format.

*  Not every parameter will be used by the designated projection.

*  If a parameter is not used the field for the parameter will be initialized to Zero.

*  All latitude and longitude fields will be specified Decimal Degree (floating point)

*  All other fields will be specified as double precision floating point values.

Please note that all co-ordinates for State Plane System contained in the Fast

Format is in map metres (not in feet).

C1(U) Universal Transverse Mercator ( UTM )

Parameter 3* 	UTM  Zone number ( Optional  )

C2(A) Albers Conical Equal Area  (  ACEA  )

Parameter 3 		Latitude of first Standard Parallel

Parameter 4		Latitude of second Standard Parallel

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C3(L) Lamberts Conformal Conic ( LCC )

Parameter 3 		Latitude of first Standard Parallel

Parameter 4		Latitude of second Standard Parallel

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C4(M) Mercator ( Mer )

Parameter 5		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	            False Northing (in metres)

C5(D)  Polar Stereographic ( PS )

Parameter 5		Longitude directed straight down below pole of map

Parameter 6 		Latitude of true scale

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C6(P)  Polyconic ( POL )

Parameter 5		Longitude of central meridian

Parameter 6 		Latitude of projection's Origin

Parameter 7		False Easting (in metres)

Parameter 8	          	False Northing (in metres)

C7(T) Tranverse Mercator ( TM )

Parameter 3 		Scale Factor at central meridian

Parameter 5		Longitude of central meridian

Parameter 6		Latitude of projections's origin

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C8(H)  Stereographic ( SG )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C9(Z)  Lamberts Azimuthal Equal Area ( LAEA )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C10(E)  Azimuthal Equidistant ( AE )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C11(G) Gnomonic ( GNO )

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C12(R) Orthographic ( OG)

Parameter 5 		Longitude of central meridian

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C13(N) General Vertical Near-Side Perspective ( GVNP )

Parameter 3		Height of perspective point above sphere

Parameter 5 		Longitude of centre of projection

Parameter 6 		Latitude of centre of projection

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C14(I) Sinusoidal  ( SIN )

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	          	False Northing (in metres)

C15(C) Miller Cylinderical ( MC)

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C16(V)  Van Der Grinten ( VDG )

Parameter 5 		Longitude of central meridian

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

C17(S) Space Oblique Mercator ( SOM )

Parameter 4                    Angle of azimuth east of north for central line

of projection

Parameter 9                    Longitude of the ascending Node

Parameter 11                  Longitude of descending Node

C18(K) Tranverse Mercator (Gauss-Krueger)( TM )

Parameter 3 		Scale Factor at central meridian

Parameter 5		Longitude of central meridian

Parameter 6		Latitude of projections's origin

Parameter 7		False Easting (in metres)

Parameter 8	           	False Northing (in metres)

# APPENDIX  - 1C : Earth Ellipsoids

This appendix contains the earth ellipsoids used in products.

| Ellipsoid Name | Semi-Major Axis (meters) | Semi-Minor Axis (meters) | Mnemonics |
| --- | --- | --- | --- |
| Clarke 1866 | 6378206.400000 | 6356583.800000 | CLARKE_1866 |
| Clarke 1880 | 6378249.145000 | 6356514.869550 | CLARKE_1880 |
| International 1967 | 63778157.500000 | 6356772.200000 | INTERNATL_1967 |
| International 1909 | 6378388.000000 | 6356911.646130 | INTERNATL_1909 |
| WGS 66 | 6378145.000000 | 6356759.769356 | WGS_66 |
| WGS 72 | 6378135.000000 | 6356750.519915 | WGS_72 |
| WGS 84 | 6378137.000000 | 6356752.314200 | WGS_84 |
| GRS 1980 | 6378137.000000 | 6356752.314140 | GRS_80 |
| Airy | 6377563.396000 | 6356256.910000 | AIRY |
| Modified Airy | 6377340.189000 | 6356034.448000 | MODIFIED_AIRY |
| Everest | 6377276.345200 | 6356075.41330 | EVEREST |
| Modified Everest | 6377304.063000 | 6356103.039000 | MODIFIED_EVEREST |
| Mercury 1960 | 6378166.000000 | 6356784.283666 | MERCURY_1960 |
| Modified Mercury 1968 | 6378150.000000 | 6356768.337303 | MOD_MERC_1968 |
| Bessel | 6377397.155000 | 6356078.962840 | BESSEL |
| Walbeck | 6376896.000000 | 6355834.846700 | WALBECK |
| Southeast Asia | 6378155.000000 | 6356773.320500 | SOUTHEAST_ASIA |
| Australian Natl. | 6378160.000000 | 6356774.719000 | AUSTRALIAN_NATL |
| Krassovsky | 6378245.000000 | 6356863.018800 | KRASSOVSKY |
| Hough | 6378270.000000 | 6356794.343479 | HOUGH |
| 6370997 Sphere | 6370997.000000 | 6370997.000000 | 6370997_M_SPHERE |

# APPENDIX  - 1D : Ellipsoid and Datum Mnemonics

| Ellipsoid Name | Ellipsoid Mnemonic | Possible Datum Name | Datum Mnemonics |
| --- | --- | --- | --- |
| Clarke 1866 | CLARKE_1866 | Datum_North_American_Datum_1927 | NAS-E |
| Clarke 1880 | CLARKE_1880 | Datum_Adindan | ADI-M |
| International 1967 | INTERNATL_1967 | Datum_New_Zealand_Geodetic_Datum_1949 | GEO |
| International 1909/1924 | INTERNATL_1909 | Datum_European_Datum_1950 | EUR-M |
| WGS 66 | WGS_66 | WGS_66 | WGS_66 |
| WGS 72 | WGS_72 | WGS_72 | WGS_72 |
| WGS 84 | WGS_84 | WGS_84 | WGS_84 |
| GRS 1980 | GRS_80 | Datum_North_American_Datum_1983 | NAR-B |
| Airy | AIRY | Datum_OSGB_1936 | OGB_M |
| Modified Airy | MODIFIED_AIRY | Datum_TM65 | IRL |
| Everest | EVEREST | Datum_Kalianpur | IND-I |
| Modified Everest | MODIFIED_EVEREST | Datum_Kalianpur | IND-I |
| Mercury 1960 | MERCURY_1960 | NOT DEFINED |  |
| Modified Mercury 1968 | MOD_MERC_1968 | NOT DEFINED |  |
| Bessel | BESSEL | Datum_Tokyo | TOY-M |
| Walbeck | WALBECK | Datum_European_Datum_1950 | EUR-M |
| Southeast Asia | SOUTHEAST_ASIA | Datum_Southasia | SOA |
| Australian Natl. | AUSTRALIAN_NATL | Datum_Australian_Geodetic_datum_1984 | AUG |
| Krassovsky | KRASSOVSKY | Datum_Pulkovo_1942 | PUK |
| Hough | HOUGH | Datum_Wake-Eniwetok_1960 | ENW |
| 6370997 Sphere | 6370997_M_SPHERE | NOT DEFINED |  |

# APPENDIX  - II: Super Structure format Layout

# Text boxes

IRS-P6

LGSOWG (Super Structure)

DIGITAL DATA PRODUCTS FORMAT

MAY, 2003

DPSD/SIPG/SIIPA

Space Applications Centre, ISRO,  Ahmedabad, INDIA.